## Slide 1: dRMT: Disaggregated Programmable Switching
Sharad Chole, Andrew Fingerhut, Sha Ma, Anirudh Sivaraman,
Shay Vargaftik, Alon Berger, Gal Mendelson, Mohammad Alizadeh,
Shang-Tse Chuang, Isaac Keslassy, Ariel Orda, and Tom Edsall
Notes: I am going to be talking about a new hardware architecture for programmable switches. This is a collaboration between many of us at Cisco, MIT, Technion, and VMWare.

## Slide 2: Today’s Programmable Switches (e.g., RMT)
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In
keys
Pkt Header
results
Pkt Header
Notes: As background, I’ll briefly review how programmable switches are architected in hardware. For concreteness, I’ll focus on the Reconfigurable Match-Action Table or RMT architecture because it is representative of many commercial products today.
Broadly, the RMT architecture is a pipeline consisting of a number of programmable pipeline stages. An operator can program the headers that are matched on in every stage and the actions carried out in response to a hit in a match-action table.
In a bit more detail, bytes come in from the wire. A parser turns these bytes into a bag of packet headers, which flows through the pipeline. Within each pipeline stage, a match unit extracts the relevant part of the packet header (out of all the packet headers) as a key for the look up in the match-action table. It then sends this to the memory cluster, which performs the lookup and returns a result. This result is used by the action unit to transform the packet headers appropriately.
This process then repeats itself.
ONLY IF YOU HAVE TIME:
One example of a key could be the destination IP address for an IP address-based forwarding lookup.
One example of an action could be setting the output port based on the result from a destination address lookup.

## Slide 3: dRMT in One Slide
RMT aggregates resources into stages that provide a fixed ratio of memory:match:action
  E.g., A large table spanning two stages consumes two match units
dRMT (disaggregated RMT): disaggregate memory, match, and action resources of a programmable switch. Allocate them independently.
Notes: The problem with RMT is that it aggregates resources into stages, which provide a fixed ratio of memory capacity (for the lookup), match key generation capacity (to generate match keys), and action capacity (to transform a limited number of action fields).
The problem with aggregating resources this way is that it is inefficient for programs that do not confirm to the fixed ratio provided by the hardware. This is because you can’t allocate resources independently. If you increase one, you have to increase the other. For instance, if you have large table that needed more memory than available in one stage, you need two stages. This also forces you to consume two match units whether you need it or not. You can’t increase memory capacity independent of match key generation capacity.
The key idea behind dRMT is to disaggregate the reesouces (match, action, and memory) of a programmable switch so that they can be allocated independently.
TODO: Instead of that example, say that “the implication of a fixed ratio => implementation of packet processing programs can be inefficient”. Could have a generic, non-specific examples. The moment you have a program that only needs a small amount of one of the resources, it gets wasted. Try to summarize it one or two sentences without a specific example.
TODO: Maybe repeat a picture of a stage with the first bullet. Show it exploding in the second bullet.

## Slide 4: The dRMT Architecture
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In
Notes: OK, what do I mean by disaggregation? Let us look at it in a bit more detail. Let’s bring back the diagram of a pipeline.

## Slide 5: Memory Disaggregation
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In
Notes: First, we disagg. memory. We replace the stage-local memory in the pipeline with a shared array of memory clusters accessible from any stage through a crossbar. Now, the stages in aggregate have access to all the memory in the system, because the memory doesn’t belong to any one stage in particular.

## Slide 6: Compute Disaggregation
Proc. 1
Proc. 2
Proc. N
Match
Action
Match
Action
Match
Action
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Distributor
Parser
In
Deparser
Pkt 1
Pkt 1
Pkt 2
Pkt 2
Pkt N
Pkt N
Notes: Next, we disaggregate compute. We replace each of the pipeline stages that is forced to execute matches followed by actions in a clumped manner with a match-action processor that can execute matches and actions in any order that respects program dependencies. Now, once packets have been parsed, they are distributed by a distributor to one of the processors in round-robin order. So the first packet goes to processor 1, the second to processor 2, and so on.
Once a processor receives a packet, it is responsible for carrying out all operations on that packet because unlike the pipeline packets don’t move around between processors. What happens to a packet once it is received by a processor? Let’s look at pkt 2 on proc 2. Over the duration of this packet, the proc might access tables in different memory clusters. Once it is done, it ships out pkt 2 and moves on to the next packet, which is N+2, because any given proc receives one packet out of N.
TODO: Action orientation here is flipped.
TODO: Save thirty seconds when talking.

## Slide 7: Compute Disaggregation
Proc. 1
Proc. 2
Proc. N
Match
Action
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Distributor
Parser
In
Deparser
Pkt 1
Match
Action
Pkt 2
Match
Action
Pkt N

## Slide 8: Compute Disaggregation
Proc. 1
Proc. 2
Proc. N
Match
Action
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Distributor
Parser
In
Deparser
Pkt 1
Match
Action
Pkt N+2
Match
Action
Pkt N
Pkt 2
Pkt 2

## Slide 9: How does dRMT improve on RMT?
Conflates memory allocation with packet processing
Example: Large table split over multiple stages
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Memory
Cluster 1
Memory
Cluster 2
Memory
Cluster 3
Stage N
Match
Action
Memory Cluster N
Must extract key multiple times
Wastes match capacity
Action units unused until last stage
dRMT will use only 1 match/action unit
Notes: Now that I have introed the dRMT architecture, let’s see what specific problems with RMT it solves. I am discussing a few here. The paper provides many more examples.
First, RMT conflate memory and packet processing resources. So if you allocate more of one, you are forced to allocate more of the other. A common example is you have a large table that is too large to fit within one memory cluster. So you split it over multiple stages. Now, to lookup a key, you look it up in each of the three partitions and decide in the last stage whether it was found anywhere and what action to carry out.
The problem with this is that it wastes match capacity because the match key is repeatedly extracted in each key to match against every partition in the table. So to perform a lookup on one table, which should require only one match key, you are forced to use three match keys just because it was a large table. Similarly, the action units are unused until the last stage because it is not clear until then, whether there was a match or not and if so, what action to carry out.
By contrast, dRMT can spread the table over multiple clusters because it is large, but still use only one match and one action unit because the memory and computational units are disaggregated in dRMT. Specifically, a single dRMT processor can generate the match key using one match unit, then multicast it over the crossbar to each of three individual units, and finally use a single action unit to carry out the action based on where the key matched.

## Slide 10: How does dRMT improve on RMT?
Suffers performance cliff if program doesn’t fit
  Recirculate packet to “extend” pipeline → Lowers throughput 2x
  dRMT’s throughput degrades gracefully as program size grows
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Stage N
Match
Action
Recirculate to ingress
Notes: The second problem with RMT is that if a program doesn’t fit, its throughput immediately degrades drastically. If a program needs more stages than provided by the switch, the only solution is to recirculate the packet back into the pipeline for a second pass. But this has the effect of cutting throughput in half. In dRMT by contrast, if a packet needs more packet processing resources, it will just stay longer at a particular processor, and we need to slow down the rate at which we send new packets to a processor, so that the queue at each proc doesn’t grow unbounded. The effect is that if you need N+1 stages instead of N, your throughput falls proportionally to N/N+1, instead of ½ as in RMT.

## Slide 11: Three Questions
Can dRMT provide deterministic throughput and latency?
Yes. Compiler schedule programs to eliminate contention using an ILP.
How does dRMT compare with RMT on real P4 programs?
Needs fewer processors on open-source, proprietary, random programs.
Are dRMT’s processors and crossbar feasible in hardware?
Yes. dRMT takes up some more area than RMT, mostly due to crossbar.
Notes: TODO: Reduce time spent on this slide.
TODO: Don’t need to spend too much time on why the questions are non obvious.
Now we’ll talk about three specific technical questions that we need to answer to determine if dRMT is practically useful.
The first is whether dRMT can provide deterministic throughput and latency for packet processing, which is a reqmt for all routers. Can dRMT provide similar guarantees? This is not obvious because there are many places where contention can arise: if two processors access the same memory on a clock cycle, one memory request may be arbitrarily delayed. Similarly, there could be variable delays if multiple operations are outstanding on a given processor.
The second question is how dRMT and RMT compare on real programs and how does a particular program affect the comparison between the two architectures? In other words, do the problems with the toy examples I presented earlier show up in real programs as well?
The third question is whether dRMT is feasible in high-speed hardware, both the dRMT processors and the crossbar, and how does it compare to a hardware implementation of RMT?
Now, let’s look at the answers.
For the first, we have built a compiler that can schedule programs to completely eliminate contention and tell a network operator at compile time what their throughput and latency will be. This scheduling problem can be posed as an integer linear program as we’ll show.
For the second, we show that we need fewer processors on open-source proprietary and randomly generated programs. The gains vary between no gains at all and 50% depending on the particular program. We can also formally show that the throughput of a program on dRMT is at least as good as that of RMT, when normalized to have the same number of hardware resources.
Finally, for the third question, we design hardware for dRMT’s processor and crossbar. We find that dRMT incurs a small amount of additional area mainly due to the crossbar.
ADD IF REQUIRED:
This architecture is very similar to a network processor or a multi-core processor where an array of processors shares access to a pool of shared memory. There are two big differences. One, the processors here have an instruction set borrowed from RMT, which gives the instructions much more parallelism than a standard processor. Second, we custom build the crossbar between processors and memories, unlike the general-purpose interconnect between procs and memories in a network processor or a multi-core processor.

## Slide 12: Compiling a P4 program to dRMT
Proc. 1
Proc. 2
Proc. N
Match
Action
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Pkt 1
Match
Action
Pkt 2
Match
Action
Pkt N
Cycle Packet | 0 | 1 | 2 | 3 | 4 | 5
1 | M |  | A | … |  | 
2 |  |  | M |  | A | …
3 |  |  |  |  | M | …
Cycle Packet | 0 | 1 | 2 | 3 | 4 | 5
1 | M |  | A | … |  | 
2 |  |  | M |  | A | …
3 |  |  |  |  | M | …
Cycle Packet | 0 | 1 | 2 | 3 | 4 | 5
1 | M |  | A | … |  | 
2 |  |  | M |  | A | …
3 |  |  |  |  | M | …
Table placement
Processor scheduling
Notes: OK. Let’s look at each of the three questions.

## Slide 13: Xbar decouples scheduling and placement
RMT couples scheduling and placement
In dRMT the crossbar decouples them.
  Assign tables to clusters; respect table sizes and xbar constraints.
  Schedule programs on processors; respect match, action, and xbar constraints.
Decoupling holds if both memory and processors respect xbar
Greatly simplifies compilation; can focus on scheduling alone.
Notes: Explain why RMT couples the two problems: memory is local to each stage.
Say that table placement is handled by prior work by Jose et al.
Say that we focus on processor scheduling here
Mention that the formal proof of decoupling is in the paper.
Explain this decoupling enough to state later that “RMT’s results are under a full disagg model”.

## Slide 14: Processor Scheduling Example
  3 cycles to complete a match
  1 cycle to complete an action
  Two processors
  Each does 1 match, 1 action per cycle
Proc. 1
Proc. 2
Match
Action
Match
Action
Program Dependencies
Resource Constraints
M0
A0
A1
M1
3
1
3
Notes: Two main aspects: correctness based on program dependencies, resource constraints based on processors.
TODO: State that it’s a very simply linear DAG. In general, it can be more complicated.

## Slide 15: Processor Scheduling Example
Cycle Pkt | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
  2 processors handle 1 packet per cycle.
  Packet arrives every 2 cycles per processor.
M0
A0
A1
M1
3
1
3

## Slide 16: Processor Scheduling Example
Cycle Pkt | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | M0 |  |  | A0 | M1 |  |  | A1 |  |  |  |  |  |  |  |  |  |  | 
  2 processors handle 1 packet per cycle.
  Packet arrives every 2 cycles per processor.
M0
A0
A1
M1
3
1
3

## Slide 17: Processor Scheduling Example
Cycle Pkt | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | M0 |  |  | A0 | M1 |  |  | A1 |  |  |  |  |  |  |  |  |  |  | 
2 |  |  | M0 |  |  | A0 | M1 |  |  | A1 |  |  |  |  |  |  |  |  | 
  2 processors handle 1 packet per cycle.
  Packet arrives every 2 cycles per processor.
M0
A0
A1
M1
3
1
3

## Slide 18: Processor Scheduling Example
Cycle Pkt | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | M0 |  |  | A0 | M1 |  |  | A1 |  |  |  |  |  |  |  |  |  |  | 
2 |  |  | M0 |  |  | A0 | M1 |  |  | A1 |  |  |  |  |  |  |  |  | 
3 |  |  |  |  | M0 |  |  | A0 | M1 |  |  | A1 |  |  |  |  |  |  | 
  2 processors handle 1 packet per cycle.
  Packet arrives every 2 cycles per processor.
M0
A0
A1
M1
3
1
3
Each processor can only do 1 match per cycle

## Slide 19: Processor Scheduling Example
Cycle Pkt | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | M0 |  |  | A0 | X | M1 |  |  | A1 |  |  |  |  |  |  |  |  |  | 
  2 processors handle 1 packet per cycle.
  Packet arrives every 2 cycles per processor.
M0
A0
A1
M1
3
1
3
Delay M1 by inserting a no-op

## Slide 20: Processor Scheduling Example
Cycle Pkt | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | M0 |  |  | A0 | X | M1 |  |  | A1 |  |  |  |  |  |  |  |  |  | 
2 |  |  | M0 |  |  | A0 | X | M1 |  |  | A1 |  |  |  |  |  |  |  | 
3 |  |  |  |  | M0 |  |  | A0 | X | M1 |  |  | A1 |  |  |  |  |  | 
  2 processors handle 1 packet per cycle.
  Packet arrives every 2 cycles per processor.
M0
A0
A1
M1
3
1
3

## Slide 21: Processor Scheduling Example
Cycle Pkt | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | M0 |  |  | A0 | X | M1 |  |  | A1 |  |  |  |  |  |  |  |  |  | 
2 |  |  | M0 |  |  | A0 | X | M1 |  |  | A1 |  |  |  |  |  |  |  | 
3 |  |  |  |  | M0 |  |  | A0 | X | M1 |  |  | A1 |  |  |  |  |  | 
4 |  |  |  |  |  |  | M0 |  |  | A0 | X | M1 |  |  | A1 |  |  |  | 
  2 processors handle 1 packet per cycle.
  Packet arrives every 2 cycles per processor.
M0
A0
A1
M1
3
1
3

## Slide 22: Processor Scheduling Example
Cycle Pkt | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | M0 |  |  | A0 | X | M1 |  |  | A1 |  |  |  |  |  |  |  |  |  | 
2 |  |  | M0 |  |  | A0 | X | M1 |  |  | A1 |  |  |  |  |  |  |  | 
3 |  |  |  |  | M0 |  |  | A0 | X | M1 |  |  | A1 |  |  |  |  |  | 
4 |  |  |  |  |  |  | M0 |  |  | A0 | X | M1 |  |  | A1 |  |  |  | 
5 |  |  |  |  |  |  |  |  | M0 |  |  | A0 | X | M1 |  |  | A1 |  | 
  2 processors handle 1 packet per cycle.
  Packet arrives every 2 cycles per processor.
M0
A0
A1
M1
3
1
3

## Slide 23: Processor Scheduling Example
Cycle Pkt | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | M0 |  |  | A0 | X | M1 |  |  | A1 |  |  |  |  |  |  |  |  |  | 
2 |  |  | M0 |  |  | A0 | X | M1 |  |  | A1 |  |  |  |  |  |  |  | 
3 |  |  |  |  | M0 |  |  | A0 | X | M1 |  |  | A1 |  |  |  |  |  | 
4 |  |  |  |  |  |  | M0 |  |  | A0 | X | M1 |  |  | A1 |  |  |  | 
5 |  |  |  |  |  |  |  |  | M0 |  |  | A0 | X | M1 |  |  | A1 |  | 
6 |  |  |  |  |  |  |  |  |  |  | M0 |  |  | A0 | X | M1 |  |  | A1
  2 processors handle 1 packet per cycle.
  Packet arrives every 2 cycles per processor.
M0
A0
A1
M1
3
1
3

## Slide 24: Minimizing no-ops: ILP formulation
Dependency constraints
Ensure schedule can be repeated every N cycles w/o violating
resource constraints:
  Create a circle with N equal sectors.
  Assign each operation op to sector (mod N).
  Enforce resource limits on all operations within a sector.
- ≥
Objective: Minimize max ti
Notes: TODO: Say why we want to minimize no-ops to minimize packet processing latency.
N sectors are not N processors. They are N periods.
Bullets are taking up too much room and detracting from the animation. Remove the three sub-bullets and make the cirle animation front and center.
Reduce text and highlight animations.
Next constraint is to repeat the schedule with period N without violating resource constraints.
Repeat the line with shifts linearly in a style similar to the tableau.
Then show the circle and make sure the sectors in the circle corresponds to columns in the repeated schedule.
Could write t_op as quotient * period + remainder.
Linear tableu right arrow circle.
In this example, we introduced a no-op, but that’s a greedy way of solving it. If we want the optimal schedule, need to solve an ILP.
Packet that arrived this scheduling period, 1 period in the past, 2 in the past, and so on.
TO stress: minimize max ti is equivalent to minimizing number of no-ops
The circle with sectors captures the intuition about operations that conflict in the tableau

## Slide 25: Evaluation: Comparing RMT and dRMT
P4 Program | RMT* | dRMT | Lower bound
switch.p4 ingress | 18 | 15 | 15
Minimum number of processors to run at 1 packet/cycle
Notes: TODO: Say that we added memory disaggregtion to RMT.

## Slide 26: Evaluation: Comparing RMT and dRMT
P4 Program | RMT* | dRMT | Lower bound
switch.p4 ingress | 18 | 15 | 15
switch.p4 egress | 12 | 7 | 7
Minimum number of processors to run at 1 packet/cycle

## Slide 27: Evaluation: Comparing RMT and dRMT
P4 Program | RMT* | dRMT | Lower bound
switch.p4 ingress | 18 | 15 | 15
switch.p4 egress | 12 | 7 | 7
switch.p4 combined | 22 | 21 | 21
Minimum number of processors to run at 1 packet/cycle

## Slide 28: Evaluation: Comparing RMT and dRMT
P4 Program | RMT* | dRMT | Lower bound
switch.p4 ingress | 18 | 15 | 15
switch.p4 egress | 12 | 7 | 7
switch.p4 combined | 22 | 21 | 21
proprietary (normalized) | 2.0 | 1.0 | 1.0
Minimum number of processors to run at 1 packet/cycle
Gains of 4.5% to 50% on real programs.
Gains low on balanced programs optimized for RMT.
On 100 random programs, mean gain of 10% (max 30%)
Notes: TODO: Maybe add a figure for random program.
Emphasize: Our gains are quite significant. Switch.p4 is optimized for RMT. We give switch.p4 the benefit of full memory disaggregation.

## Slide 29: dRMT eliminates performance cliffs
Chart: Processors
| 1.0 | 1.0 | 2.0 | 2.0 | 3.0 | 3.0 | 4.0 | 4.0 | 5.0 | 5.0 | 6.0 | 6.0 | 7.0 | 7.0 | 8.0 | 8.0 | 9.0 | 9.0 | 10.0 | 10.0 | 11.0 | 11.0 | 12.0 | 12.0 | 13.0 | 13.0 | 14.0 | 14.0 | 15.0 | 15.0
RMT | 0.08 | 0.083333 | 0.083333 | 0.16667 | 0.16667 | 0.25 | 0.25 | 0.33 | 0.33 | 0.33 | 0.33 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 1 | 1 | 1 | 1 | 1 | 1 | 1
dRMT | 0.14 | 0.29 | 0.43 | 0.57 | 0.71 | 0.86 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 30: dRMT Hardware Feasibility
dRMT processor
  Match unit and action unit are similar to an RMT stage.
  dRMT processor executes and stores entire program.
  RMT stage only executes and stores a fragment.
  Need to optimize a dRMT processor to be area competitive with RMT.
dRMT crossbar
  Must connect every processor key to every memory cluster key
  Wiring complexity goes up quadratically with the number of processors
  New design, manual place-and-route scales crossbar to 32 processors
  Crossbar is the main limiting factor; seems hard to scale further

## Slide 31: Comparing areas of RMT and dRMT
dRMT incurs a few mm2 additional area.
Modest in comparison to a 300-700 mm2 chip.
Chart: Processors/Stages
| 16.0 | 24.0 | 32.0
RMT | 19.9 | 29.9 | 39.8
dRMT | 22.7 | 34.1 | 45.5
Notes: Say that the area is mostly dominated by IO and memories.
TODO: Break up dRMT’s area by crossbar and the rest.

## Slide 32: Conclusion
Disaggregation improves flexibility
  Improves hardware utilization
  More complex programs on the same hardware
  Less hardware for the same program
Ongoing: Silicon implementation of dRMT in programmable NIC
Webpage: http://drmt.technion.ac.il/

## Slide 33: Backup slides

## Slide 34: dRMT crossbar design
Proc. 1
Crossbar needs to send multiple match keys from processors to clusters every clock cycle
Two extremes
Mem. 1
Mem. 2
Proc. 2
Full crossbar connecting
every processor key to
every memory key
Very flexible,
but too many wires
(4 keys * 4 keys = 16).

## Slide 35: dRMT crossbar design
Crossbar needs to send multiple match keys from processors to clusters every clock cycle
Two extremes
Unit crossbar connecting
every processor to every memory
Rigid (all proc. keys go to same mem.)
but cheap to build
(2 proc *2 mems * 2 keys per wire =8)
Proc. 1
Mem. 1
Mem. 2
Proc. 2

## Slide 36: dRMT crossbar design
Crossbar needs to send multiple match keys from processors to clusters every clock cycle
dRMT’s crossbar: 2 parallel crossbars, one per key (8 wires)
Proc. 1
Mem. 1
Mem. 2
Proc. 2
Proc. 1
Mem. 1
Mem. 2
Proc. 2
Left key
Right key

## Slide 37: dRMT’s crossbar
dRMT’s crossbar has wire count similar to unit crossbar
But a processor can send keys to different memories by call one the left and the other right.
Equivalent to full if tables are not split across clusters.
Scales to 32 processors, 32 memories, 8 keys through manual place and route.
Notes: Say that if tables are split, it’s no longer equivalent, which means the previously decoupled problems become coupled.

## Slide 38: Evaluation: switch.p4 on RMT and dRMT
P4 Program | RMT | dRMT | Lower bound
Ingress (switch.p4) | 18 | 15 | 15
Egress (switch.p4) | 12 | 7 | 7
Switch.p4 combined | 22 | 21 | 21
Minimum number of processors to run at 1 packet/cycle
P4 Program | RMT | dRMT (IPC=2) | Lower bound
Ingress (switch.p4) | 360 | 243 | 243
Egress (switch.p4) | 240 | 198 | 197
Switch.p4 combined | 440 | 243 | 243
Minimum number of threads to run at 1 packet/cycle
Notes: Switch.p4 is optimized for RMT.
198 in red is distracting.
Explain briefly what switch.p4 is.
Explain why ingress+egress is not the same as combined.
Explain why combined is not a huge win.
The results seem comparable, not better for dRMT.

## Slide 39: Evaluation: switch.p4 on RMT and dRMT
P4 Program | RMT | dRMT (IPC=1) | dRMT (IPC=2) | Lower bound
Ingress (switch.p4) | 18 | 17 | 15 | 15
Egress (switch.p4) | 12 | 11 | 7 | 7
Switch.p4 combined | 22 | 21 | 21 | 21
Minimum number of processors to run at 1 packet/cycle
P4 Program | RMT | dRMT (IPC=1) | dRMT (IPC=2) | Lower bound
Ingress (switch.p4) | 360 | 245 | 243 | 243
Egress (switch.p4) | 240 | 217 | 198 | 197
Switch.p4 combined | 440 | 243 | 243 | 243
Minimum number of threads to run at 1 packet/cycle
dRMT is near optimal:
Fewest possible processors
Near-ideal (critical path) latency
Comparable on switch.p4 combined, which is optimized for RMT
Notes: Switch.p4 is optimized for RMT.
198 in red is distracting.
Explain briefly what switch.p4 is.
Explain why ingress+egress is not the same as combined.
Explain why combined is not a huge win.
The results seem comparable, not better for dRMT.

## Slide 40: Scheduling Constraints
Processor resource constraints:
Generate up to M b-bit keys to match on per cycle (M=8, b=80)
  Perform actions on up to A packet fields per cycle (A=32)
  Perform match/action on different packets every cycle (Inter-packet concurrency (IPC) = 1 or 2)
Dependency constraints:
  Operation depending on a match (action) has to wait dM (or dA) cycles
Notes: Change this into compiler overview and add a overview diagram P4->DAG->Packet Scheduling. Also simplify constraints. Maybe show constraints in the overview diagram.
TODO: Bring back diagram of the processor to explain
IPC went by too fast. Need to introduce it so that people are not lost. Maybe just call it packet concurrency?
Multi-processor design can lead to reordering. Useful to mention this is not a problem up front because everything has the same latency.
Too much redundancy in the second bullet
TODO: More animations here
Too many details
It wasn’t clear what a key was.
Too many details.
Simplify number of constraints.

## Slide 41: Extracting dependencies from P4 programs
Table dependency graph
Operation dependency graph
Routable
Match
Multicast
Match
IGMP
Match
Routable
Action
Multicast
Action
IGMP
Action
dM
dA
dM
dM
dA
Match
Dep.
Action
Dep.
Routable
Multicast
IGMP
Notes: This leads into the compiler.
Toy example very loosely inspired by L2-L3 with Multicast.
TODO: Might be too detailed.
This part was not very interesting here.
Didn’t get the high-level problem in slide 15. Make it very clear what proc. Scheduling was on slide 15.
Say that you go from P4->Operation dependency graph -> ILP (and then you could say that the P4->ODG transformation is not shown).
Could remove this slide.

## Slide 42: dRMT hardware: instruction memory
A dRMT processor executes/stores an entire program; an RMT stage only executes/stores a program slice.
Must reduce memory required to encode an action.
RMT actions can modify 224 packet fields in parallel; we found 32 sufficient
Chart: Distribution of number of packet fields in switch.p4 actions
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 10.0 | 14.0 | 18.0 | 21.0 | 25.0 | 29.0
Number of primitive actions to execute | 0.056452 | 0.25806 | 0.16935 | 0.15323 | 0.10484 | 0.024194 | 0.032258 | 0.056452 | 0.056452 | 0.040323 | 0.0080645 | 0.016129 | 0.0080645 | 0.0080645 | 0.0080645
Notes: Mention that the lower half is a histogram or empirical distribution
The pdf indicates 29 is sufficient, but you seem to have 32.
Seemed like a jump from eval to design (hardware design)
Some sign posting would help.
Make it clear that the processor has to store the program.

## Slide 43: dRMT architecture: crossbar
The segment crossbar is equivalent to full crossbar if tables are not split across clusters! (see paper for details)
dRMT uses One-to-Many Segment Crossbar
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Unit Crossbar
(0.561 mm2)
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Segment Crossbar
(0.576 mm2)
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Full Crossbar
(4.464 mm2)
Notes: Area numbers for 32x32 crossbar with 8 80-bit keys on each side

## Slide 44: dRMT Match Action Processor
Packet Header Vector
(4Kb)
Packet Header Vector
(4Kb)
Packet Header Vector
(4Kb)
Crossbar to
Memories
Scratch
Pad
8x80b Key
Action Input Selector
(crossbar)
Config
Table
Action Output Selector
(crossbar)
VLIW Instruction Table
Ctrl
Thread Select
8x96b Action
Memory
Match Key Generation (crossbar)
ALU
ALU
Op code
… …
Notes: TODO: This diagram might be too detailed.
Maybe just replace it with a high-level overview slide.
Key differences with RMT:
-- dRMT processor needs to store full program  Config table & instruction table more expensive
-- Scratchpad (store results for delayed execution
-- VLIW Instructions: 32 ALUs instead of 224

## Slide 45: Enforcing periodic resource constraints
Indicator variables I[op, q, r] denote whether top has quotient q and remainder r when divided by N
=
dividend = divisor * quotient + remainder
= 1 (for each op)
q, r are unique
<= A (for each r)
action constraints are not violated (match constraints similar)

## Slide 46: Problems with RMT Architecture
Forces rigid order on operations: match→action→match→action→…
  Wastes resources for “imbalanced” programs
Example: Tables without a match (default action)
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Stage N
Match
Action
Default action
Notes: TODO: Consider removing slide on tables without a match. Technically, we can pack this with another program that *does* use the match. i.e., could combine slide 4 with slide 3.