## Slide 1: dRMT: Disaggregated Programmable Switching
Sharad Chole, Andrew Fingerhut, Sha Ma, Anirudh Sivaraman, Shay Vargaftik, Alon Berger, Gal Mendelson, Mohammad Alizadeh, Shang-Tse Chuang, Isaac Keslassy, Ariel Orda, and Tom Edsall
Notes: TODO: Prioritize changes to the compilation part of the talk (compilation + sub-problems + fine-grained deps + proc constraints + animation)

## Slide 2: Today’s Programmable Switches (e.g., RMT)
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In
keys
Pkt Header
results
Pkt Header
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 3: Problems with RMT Architecture
Conflates memory allocation with packet processing
  Wastes processing and/or memory resources
Example: Large table split over multiple stages
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Memory Cluster 1
Memory Cluster 2
Memory Cluster 3
Stage N
Match
Action
Memory Cluster N
Must extract key multiple times
Only last stage executes action
Wastes match/action capacity
Notes: Large table:
* Each stage has to extract and search for the key
* Action cannot be executed until last stage
 Wastes key generation and action capacity

## Slide 4: Problems with RMT Architecture
Forces rigid order on operations: match→action→match→action→…
  Wastes resources for “imbalanced” programs
Example: Tables without a match (default action)
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Stage N
Match
Action
Default action
Notes: Large table:
* Each stage has to extract and search for the key
* Action cannot be executed until last stage
 Wastes key generation and action capacity

## Slide 5: Problems with RMT Architecture
Suffers performance cliff if program doesn’t fit
  Recirculate packet to “extend” pipeline → Lowers throughput 2x
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Stage N
Match
Action
Recirculate to ingress
Notes: Large table:
* Each stage has to extract and search for the key
* Action cannot be executed until last stage
 Wastes key generation and action capacity

## Slide 6: Problems with RMT Architecture
Conflates memory allocation with packet processing
Forces rigid order on operations (match→action→match→action→ …)
Suffers performance cliff if program doesn’t fit
The dRMT architecture solves all 3 problems
Key idea:
Disaggregate hardware resources of a programmable switch

## Slide 7: The dRMT Architecture
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 8
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 9
Proc. 1
Proc. 2
Proc. N
Match
Action
Match
Action
Match
Action
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Distributor
Parser
In
Deparser
Pkt 1
Pkt 1
Pkt 2
Pkt 2
Pkt N
Pkt N
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 10
Proc. 1
Proc. 2
Proc. N
Match
Action
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Distributor
Parser
In
Deparser
Pkt 1
Match
Action
Pkt 2
Match
Action
Pkt N
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 11
Proc. 1
Proc. 2
Proc. N
Match
Action
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Distributor
Parser
In
Deparser
Pkt 1
Match
Action
Pkt N+2
Match
Action
Pkt N
Pkt 2
Pkt 2
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 12: dRMT solves problems with RMT
RMT Conflates memory allocation with packet processing
dRMT decouples memory and processors via crossbar
RMT forces rigid order on operations
dRMT enables arbitrary order for operations
RMT suffers performance cliff if program doesn’t fit (recirculation)
dRMT’s throughput degrades gracefully as program size grows

## Slide 13: Two Key Questions
Can dRMT provide deterministic performance?
  Contention at processors, memories, processor/memory interconnect, etc.
Yes! We can preschedule system at compile time to prevent contention entirely.
How much does it cost to build?
  Processor and crossbar area, wiring complexity, etc.
Hardware costs are comparable to RMT. (But dRMT utilizes hardware resources more efficiently.)
Notes: The rest of the talk will look at these questions in more depth.

## Slide 14: Compiling a P4 program to dRMT
Table Placement
Processor scheduling
Crossbar decouples the two problems
Match
Action
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Match
Action
Match
Action
Proc. 1
Proc. 2
Proc. N
?
?
?
Notes: TODO: Maybe add a figure here.

## Slide 15: Scheduling Constraints
Processor resource constraints:
Generate up to M b-bit keys to match on per cycle (M=8, b=80)
  Perform actions on up to A packet fields per cycle (A=32)
  Perform match/action on IPC packets per cycle (IPC=1 or 2)
Dependency constraints:
  Operation depending on a match has to wait dM cycles (dM=22)
  Operation depending on an action has to wait dA cycles (dA=2)
Notes: TODO: Bring back diagram of the processor to explain

## Slide 16: Modeling dependencies
Table dependency graph
Operation dependency graph
Routable
Match
Multicast
Match
IGMP
Match
Routable
Action
Multicast
Action
IGMP
Action
dM
dA
dM
dM
dA
Match
Dep.
Action
Dep.
Routable
Multicast
IGMP
Notes: This leads into the compiler.
Toy example very loosely inspired by L2-L3 with Multicast.

## Slide 17: Scheduling Example
M0
A0
A1
1
1
1
M1
1
2
1
1
  Each match → 1 key
  Each action → 1 field
  dM (Match latency) = 2 cycles
  dA (Action latency) = 1 cycles
  N = 2 processors
  M (Match capacity) = 1 key per cycle
  A (Action capacity) = 1 field per cycle
  IPC (Concurrency) = 1 pkt per cycle
Proc. 1
Proc. 2
Match
Action
Match
Action

## Slide 18: Scheduling Example
  Focus on 1 processor
  1 packet arrives every 2 cycles
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 19: Scheduling Example
  Focus on 1 processor
  1 packet arrives every 2 cycles
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 20: Scheduling Example
  Focus on 1 processor
  1 packet arrives every 2 cycles
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  | 
Violates action capacity
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 21: Scheduling Example
  Focus on 1 processor
  1 packet arrives every 2 cycles
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | X | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | X | A1 |  |  |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 22: Scheduling Example
  Focus on 1 processor
  1 packet arrives every 2 cycles
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | X | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | X | A1 |  |  |  |  |  | 
 |  |  |  |  | M0 |  | A0 | M1 | X | A1 |  |  |  | 
 |  |  |  |  |  |  | M0 |  | A0 | M1 | X | A1 |  | 
 |  |  |  |  |  |  |  |  | M0 |  | A0 | M1 | X | A1
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 23: ILP formulation of scheduling problem
Assign each operation start time
Objective: Minimize max ti
Dependency constraints
Ensure schedule can be repeated every N cycles w/o violating
resource constraints:
  Create a circle with N equal sectors,
  Assign each operation op to sector (mod N),
  Enforce resource limits on all operations within a sector
- ≥
Notes: In this example, we introduced a no-op, but that’s a greedy way of solving it. If we want the optimal schedule, need to solve an ILP.

## Slide 24: Enforcing periodic resource constraints
Indicator variables I[op, q, r] denote whether top has quotient q and remainder r when divided by N
=
dividend = divisor * quotient + remainder
= 1 (for each op)
q, r are unique
<= A (for each r)
action constraints are not violated (match constraints similar)

## Slide 25: Evaluation: switch.p4 on RMT and dRMT
P4 Program | RMT | dRMT (IPC=1) | dRMT (IPC=2) | Lower bound
Ingress (switch.p4) | 18 | 17 | 15 | 15
Egress (switch.p4) | 12 | 11 | 7 | 7
Switch.p4 combined | 22 | 21 | 21 | 21
Minimum number of processors to run at 1 packet/cycle
P4 Program | RMT | dRMT (IPC=1) | dRMT (IPC=2) | Lower bound
Ingress (switch.p4) | 360 | 245 | 243 | 243
Egress (switch.p4) | 240 | 217 | 198 | 197
Switch.p4 combined | 440 | 243 | 243 | 243
Minimum number of threads to run at 1 packet/cycle
dRMT is near optimal; to run at line-rate:
Fewest possible processors
Near-ideal (critical path) latency
Notes: Switch.p4 is optimized for RMT.

## Slide 26: dRMT eliminates performance cliffs
Throughput vs. Processors for switch.p4 egress

## Slide 27: dRMT Match Action Processor
Packet Header Vector
(4Kb)
Packet Header Vector
(4Kb)
Packet Header Vector
(4Kb)
Crossbar to
Memories
Scratch
Pad
8x80b Key
Action Input Selector
(crossbar)
Config
Table
Action Output Selector
(crossbar)
VLIW Instruction Table
Ctrl
Thread Select
8x96b Action
Memory
Match Key Generation (crossbar)
ALU
ALU
Op code
… …
Notes: Key differences with RMT:
-- dRMT processor needs to store full program  Config table & instruction table more expensive
-- Scratchpad (store results for delayed execution
-- VLIW Instructions: 32 ALUs instead of 224

## Slide 28: Crossbar designs
The segment crossbar is equivalent to full crossbar if tables are not split across clusters! (see paper for details)
dRMT uses One-to-Many Segment Crossbar
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Unit Crossbar
(0.561 mm2)
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Segment Crossbar
(0.576 mm2)
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Full Crossbar
(4.464 mm2)
Notes: Area numbers for 32x32 crossbar with 8 80-bit keys on each side

## Slide 29: Hardware area estimates (mm2)
Number of Processors | RMT | Crossbar with 32 memory clusters | dRMT(IPC=1) with crossbar | dRMT(IPC=2) with crossbar
16 | 19.9 | 0.857 | 17.7 | 22.7
24 | 29.9 | 1.254 | 26.6 | 34.1
32 | 39.8 | 1.740 | 35.5 | 45.5
dRMT hardware cost is comparable to RMT.

## Slide 30: Summary
dRMT: Disaggregated architecture for programmable switches
Paper appearing at SIGCOMM 2017
Ongoing work: Implementation in programmable NIC
Lots of interesting open questions
  Scheduling different packet types
  Stateful packet processing

## Slide 32: Problems with RMT Architecture
Conflates memory allocation with packet processing
  Wastes processing and/or memory resources
Example: Parallel table lookups that exceed key gen. capacity of a stage
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Memory Cluster 1
Memory Cluster 2
Memory Cluster 3
Stage N
Match
Action
Memory Cluster N
Must spread tables across multiple stages
Wastes memory capacity

## Slide 33: Compiling a P4 program to dRMT
Memory: Allocate logical tables to memory clusters
Compute: Schedule processors respecting resource and dependency constraints
Joint optimization problem in general
  Crossbar decouples the memory and compute problems
    Compute schedule must satisfy crossbar constraints on processor side
    Table placement must satisfy crossbar constraints on memory side
Notes: TODO: Maybe add a figure here.

## Slide 34: Evaluation: Key questions
How efficiently can dRMT utilize hardware resources?
Minimum number of processors/threads to run a P4 program at line-rate
What happens when hardware resources are insufficient?
Throughput as a function of the number of processors
Is it feasible?
Area cost of dRMT vs. RMT

## Slide 35: Summary
Disaggregated flexible architecture for high speed programmable switching
Higher resource utilization
  Lower latency
  Lower thread count
Graceful degradation of throughput
Independent scaling of processing/memory capacity
Applications:
Low Latency Switching
SmartNIC
Off-chip buffers/non-deterministic memory latencies

## Slide 36: Hardware costs
Hardware area in 16 nm excluding wires and memory
  32-stage RMT: 39.8 square mm
  32-processor dRMT (32-wide VLIW, segment crossbar): 45.5 square mm
  Of the 45.5, 1.74 is due to the crossbar, the rest due to 32 dRMT cores
Tentative analysis is that hardware costs are comparable
  Tentative because RMT’s numbers are based on 28 nm
Notes: TODO: Maybe mention thread count.

## Slide 37: Crossbar requirements
Need to connect 32 processors to 32 memory clusters
Each processor can generate up to 8 match keys
Each memory cluster can receive up to 8 match keys
Need multicasting for large tables spread out over multiple memories

## Slide 38: Crossbar designs
Three possible crossbars:
  Unit crossbar: 32*32 crossbar with width to support 8 keys: too restrictive
  Full crossbar: (32 * 8) * (32 * 8) crossbar: too expensive to build
  Segment crossbar: 8 parallel (32*32) crossbars: feasible, with little loss in expressiveness (if tables aren’t split across clusters, equivalent to full)
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Unit Crossbar
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Full Crossbar
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Segment Crossbar

## Slide 39: Differences in architecture relative to RMT
Unlike RMT, each dRMT processor needs to store full program
Unlike RMT, we need a scratch pad to store action results for delayed execution
Need to optimize hardware design
  Reduce the number of parallel action fields in a single VLIW from 224 to 32
  Empirically sufficient on switch.p4
Notes: Hardware analysis takeaways:

## Slide 40: dRMT eliminates performance cliffs
Chart: Throughput of switch.p4 egress as the number of processors decreases
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0
RMT | 0.083333 | 0.16667 | 0.25 | 0.33333 | 0.33333 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 1
dRMT | 0.14286 | 0.28571 | 0.42857 | 0.57143 | 0.71429 | 0.85714 | 1 | 1 | 1 | 1 | 1
dRMT’s performance degrades gracefully

## Slide 41: Results: switch.p4 on RMT and dRMT
Program | RMT | dRMT | Lower Bound
Ingress | 18 | 15 | 15
Egress | 12 | 7 | 7
Combined | 22 | 21 | 21
Number of processors/stages to run switch.p4 at 1 packet/cycle
dRMT’s gains are most when the program is imbalanced
Notes: Switch.p4 is optimized for RMT.

## Slide 42: Hardware design for dRMT
()
Packet Header Vector
(4Kb)
VLIW Instruction Table
Config
Table
Crossbar to
Memories
ALU
Thread Select
Scratch
Pad
640b Key
Action Input Selector
(crossbar)
ALU
Action Output Selector
(crossbar)
Op code
Ctrl
… …
8x96b Action
Memory
Match Key Generation (crossbar)

## Slide 43: Ongoing and future work
Ongoing work: Implementation in programmable NIC
Future work: State modifications in dRMT
  Run-to-completion allows us to spread state modifications over multiple clock cycles

## Slide 44: Problems with RMT Architecture
Conflates memory allocation with packet processing
  Wastes processing and/or memory resources
Example: Parallel table lookups that exceed key gen. capacity of a stage
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Memory Cluster 1
Memory Cluster 2
Memory Cluster 3
Stage N
Match
Action
Memory Cluster N
Must spread tables across multiple stages
Wastes memory capacity

## Slide 45: Related Work
Network processors (IXP, Netronome, Quantum Flow)
  Run-to-completion
  Shared memory
  X86-like instructions
  Caches,
  Memory hierarchies,
  General-purpose interconnects,
  Hard to provide determinism
dRMT
Run-to-completion
Shared memory
VLIW instructions with more parallelism
No caches
Single level of memory
Custom crossbar
Compiler solves ILP to provide deterministic latency

## Slide 46: Hardware Implementation
Key Differences:
Match Action Processor
  Packet Contexts
  Scratch pad
VLIW Instructions
Crossbar

## Slide 47: Match-Action Processor
Packet Header Vector
(4Kb)
Packet Header Vector
(4Kb)
Packet Header Vector
(4Kb)
Crossbar to
Memories
Scratch
Pad
8x80b Key
Action Input Selector
(crossbar)
Config
Table
Action Output Selector
(crossbar)
VLIW Instruction Table
Ctrl
Thread Select
8x96b Action
Memory
Match Key Generation (crossbar)
ALU
ALU
Op code
… …

## Slide 48: VLIW Instructions
Over 90% of tables require 8 or fewer primitive actions.
dRMT implements 32 of 32-bit ALUs
Instruction memory is implemented as 32 of 1K deep SRAMs
Chart: Switch.p4 Analysis
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 10.0 | 14.0 | 18.0 | 21.0 | 25.0 | 29.0
Number of primitive actions to execute | 0.056452 | 0.25806 | 0.16935 | 0.15323 | 0.10484 | 0.024194 | 0.032258 | 0.056452 | 0.056452 | 0.040323 | 0.0080645 | 0.016129 | 0.0080645 | 0.0080645 | 0.0080645
1K
SRAM
(for ALU 0)
1K
SRAM
(for ALU 31)
32 X 96b
ALU Select Table
Action Program
Counter
Bits[95:93]
Instruction Ptr 0 (10b)
… …
8:1 mux
Instruction Ptr 7 (10b)
Instruction Ptr 0 (10b)
… …
8:1 mux
Instruction Ptr 7 (10b)
…
Bits[2:0]

## Slide 49: Crossbar choices
The segment crossbar is as powerful as full crossbar if
  No tables are split across clusters
  Total key-segments per cluster < Max Key Segments per cluster
dRMT uses One-to-Many Segment Crossbar.
Proc. 1
Mem. 1
Proc. 1
Mem. 1
Unit Crossbar
(0.561 mm2)
Proc. 1
Mem. 1
Proc. 1
Mem. 1
Segment Crossbar
(0.576 mm2)
Proc. 1
Mem. 1
Proc. 1
Mem. 1
Full Crossbar
(4.464 mm2)

## Slide 50: Hardware Evaluation
Component | RMT | dRMT(IPC=1) | dRMT(IPC=2)
Key Generation |  |  | 
Config Register | 0.007 | 0.004 | 0.005
Key Crossbar | 0.098 | 0.049 | 0.071
Packet Storage |  |  | 
Header Vector | 0.110 | 0.326 | 0.470
Scratch Pad | N/A | 0.051 | 0.051
Actions |  |  | 
Input Crossbar | 0.486 | 0.171 | 0.315
ALUs | 0.170 | 0.071 | 0.071
Output Crossbar | N/A | 0.048 | 0.048
VLIW Table | 0.372 | 0.336 | 0.336
Total | 1.243 | 1.056 | 1.367
Estimated area per processor (mm2)

## Slide 51: Hardware Evaluation
Number of Processors | RMT | Crossbar with 32 memory clusters | dRMT(IPC=1) with crossbar | dRMT(IPC=2) with crossbar
16 | 19.9 | 0.857 | 17.7 | 22.7
24 | 29.9 | 1.254 | 26.6 | 34.1
32 | 39.8 | 1.740 | 35.5 | 45.5
a) Area of all processors plus interconnect (mm2)
Number of Processors | Power for Crossbar with 32 memory clusters
16 | 0.88 W
24 | 1.31 W
32 | 1.75 W
b) Crossbar Power @1.2 GHz 0.9V