## Slide 1: dRMT: Disaggregated Programmable Switching
Sharad Chole, Andrew Fingerhut, Sha Ma, Anirudh Sivaraman, Shay Vargaftik, Alon Berger, Gal Mendelson, Mohammad Alizadeh, Shang-Tse Chuang, Isaac Keslassy, Ariel Orda, and Tom Edsall
Notes: TODO: Prioritize changes to the compilation part of the talk (compilation + sub-problems + fine-grained deps + proc constraints + animation)

## Slide 2: Programmable Switches (e.g., RMT)
Match
Action
Memory
Match
Action
Memory
Match
Action
Memory
Stage 1
Stage 2
Stage N
Notes: TODO: Show packet flow as well through both architectures.

## Slide 3: Today’s Programmable Switches (e.g., RMT)
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Memory Cluster 1
Memory Cluster 2
Memory Cluster 3
Stage N
Match
Action
Memory Cluster N
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 4: Two Problems
RMT Conflates memory allocation with packet processing
  Example: large match-action table split over multiple stages
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Memory Cluster 1
Memory Cluster 2
Memory Cluster 3
Stage N
Match
Action
Memory Cluster N
Notes: Large table:
* Each stage has to extract and search for the key
* Action cannot be executed until last stage
 Wastes key generation and action capacity

## Slide 5: Today’s Programmable Switches (e.g., RMT)
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In
keys
Pkt Header
results
Pkt Header
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 6: Problems with RMT Architecture
RMT Conflates memory allocation with packet processing
  Wastes processing and/or memory resources
Example: Large table split over multiple stages
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Memory Cluster 1
Memory Cluster 2
Memory Cluster 3
Stage N
Match
Action
Memory Cluster N
Must extract key multiple times
Only last stage executes action
Wastes match/action capacity
Notes: Large table:
* Each stage has to extract and search for the key
* Action cannot be executed until last stage
 Wastes key generation and action capacity

## Slide 7: Problems with RMT Architecture
RMT Conflates memory allocation with packet processing
  Wastes processing and/or memory resources
Example: Parallel table lookups that exceed search key capacity of a stage
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Memory Cluster 1
Memory Cluster 2
Memory Cluster 3
Stage N
Match
Action
Memory Cluster N
Must spread tables across stages
Wastes memory capacity
Notes: Large table:
* Each stage has to extract and search for the key
* Action cannot be executed until last stage
 Wastes key generation and action capacity

## Slide 8: Problems with RMT Architecture
RMT forces rigid match-then-action order on operations
Notes: Large table:
* Each stage has to extract and search for the key
* Action cannot be executed until last stage
 Wastes key generation and action capacity

## Slide 9: Resources are aggregated in RMT
RMT couples memory allocation with computations
  Example 1: large match-action table split over multiple stages
  Action can’t execute until last stage; preceding action units unused
Forces match, followed by action order on operations
  Example 2: default actions, match capacity is wasted
Notes: TODO: Is the performance cliff really a result of aggregation?
TODO: Visual of example 1 and maybe example 2.

## Slide 10: dRMT: disaggregated RMT
Match
Action
Memory
Match
Action
Memory
Match
Action
Memory
Stage 1
Stage 2
Stage N

## Slide 11: dRMT: shared memory using crossbar
Match
Action
Memory
Match
Action
Memory
Match
Action
Memory
Stage 1
Stage 2
Stage N

## Slide 12: dRMT: run-to-completion processors
Match
Action
Memory
Match
Action
Memory
Match
Action
Memory
Packet distributor
Processor 1
Processor 2
Processor N
Notes: TODO: packet flow in run-to-completion
1. State memory layout – processing decoupling as a benefit

## Slide 13: Compiling a P4 program to dRMT
Memory : Allocating tables to memory clusters
Compute: Schedule matches, actions, respecting dependencies
In general, this is a joint optimization problem.
  But, allocation and scheduling can be done independently for round-robin schedules
Memory allocation is essentially bin packing; focus on compute scheduling
Notes: TODO: Maybe add a figure here.

## Slide 14: Compiling: fine-grained dependencies in dRMT
Table dependency graph in RMT
Operation dependency graph in dRMT
Routable
Multicast
IGMP
Match
Dep.
Action
Dep.
Routable
Match
Multicast
Match
IGMP
Match
Routable
Action
Multicast
Action
IGMP
Action
Match
latency
Action
latency
Match
latency
Match
latency
Action
latency
Notes: This leads into the compiler.

## Slide 15: dRMT resource constraints
Match limits: Each processor can generate up to M b-bit-width keys to match against tables stored in memory.
Action limits: Each processor can modify up to A packet fields in parallel.
Each table match takes dM clock cycles
Each action takes dA clock cycles
Notes: TODO: Bring back diagram of the processor to explain

## Slide 16: Animation of scheduling problem
M0
A0
A1
1
1
1
M1
1
2
1
1
N = 2 processors.
Each processor handles a new packet every 2 clock cycles
M = 1 (1 match key)
A = 1 (1 field)
dM (Match latency) = 2 clock cycles
dA (Action latency) = 1 clock cycles

## Slide 17: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 18: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1
After dependency constraints alone

## Slide 19: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1
Violates
Action
Capacity

## Slide 20: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 21: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 22: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  | 
 |  |  |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 23: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  | 
 |  |  |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  | 
 |  |  |  |  |  |  | M0 |  | A0 | M1 | x | A1 |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 24: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  | 
 |  |  |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  | 
 |  |  |  |  |  |  | M0 |  | A0 | M1 | x | A1 |  | 
 |  |  |  |  |  |  |  |  | M0 |  | A0 | M1 | x | A1
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 25: The general compilation problem
Two main constraints:
  1. Dependency constraints between operations
  2. Periodic resource constraints: Each processor handles a new packet every N cycles. Ensure schedule can be repeated every N cycles without violating resource constraints
Can be formulated as an ILP
Notes: We are going to assume one packet per clock cycle. It’s easy to extend it to more general throughputs.
TODO: Replace all the text with a figure.

## Slide 26: ILP formulation
Dependency constraints
Periodic resource constraints:
  Fold line into a circle with N equal sectors,
  assign each ti to sector (ti mod N),
  enforce resource limits on all operations within a sector
tn = Sum_(q,r)((q * N + r) * I[n, q, r]), I[n, q, r] are indicators
  S.t. Sum_(q, r) I[n, q, r] = 1 (q, r are unique)
  S.t. Sum_(n,q)a(n)*I[n, q, r] <= A (action limits are not violated)
t1
t0
t2
t3
t4
t2 – t1 >= e(1,2)
t0
t1
t2
t3
t4

## Slide 27: Results: switch.p4 on RMT and dRMT
Program | RMT | dRMT | Lower Bound
Ingress | 18 | 15 | 15
Egress | 12 | 7 | 7
Combined | 22 | 21 | 21
Minimum number of processors/stages to run switch.p4 at 1 packet per cycle
dRMT’s gains are most when the program is imbalanced in terms of matches and actions
Combining balances matches and actions and favors RMT
Notes: Switch.p4 is optimized for RMT.

## Slide 28: dRMT eliminates performance cliffs
Chart: Throughput of switch.p4 egress as the number of processors decreases
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0
RMT | 0.083333 | 0.16667 | 0.25 | 0.33333 | 0.33333 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 1
dRMT | 0.14286 | 0.28571 | 0.42857 | 0.57143 | 0.71429 | 0.85714 | 1 | 1 | 1 | 1 | 1

## Slide 29: Hardware design for dRMT
()
Packet Header Vector
(4Kb)
VLIW Instruction Table
Config
Table
Crossbar to
Memories
ALU
Thread Select
Scratch
Pad
640b Key
Action Input Selector
(crossbar)
ALU
Action Output Selector
(crossbar)
Op code
Ctrl
… …
8x96b Action
Memory
Match Key Generation (crossbar)

## Slide 30: Differences in hardware from RMT
Unlike RMT, each dRMT processor needs to store full program
Unlike RMT, we need a scratch pad to store action results for delayed execution
Need to optimize hardware design
  Reduce the number of parallel action fields in a single VLIW from 224 to 32
  Empirically sufficient on switch.p4
  If not, spread action over multiple cycles
Notes: Hardware analysis takeaways:

## Slide 31: Crossbar analysis
Need to connect 32 processors to 32 memory clusters
Each processor can generate up to 8 match keys
Each memory cluster can receive up to 8 match keys
Need multicasting for large tables spread out over multiple memories

## Slide 32: Crossbar designs
Three possible crossbars:
  Unit crossbar: 32*32 crossbar with width to support 8 keys: too restrictive
  Full crossbar: (32 * 8) * (32 * 8) crossbar: too expensive to build
  Segment crossbar: 8 parallel (32*32) crossbars: feasible, with little loss in expressiveness (if tables aren’t split across clusters, equivalent to full)
Proc. 1
Mem. 1
Proc. 1
Mem. 1
Proc. 1
Mem. 1
Proc. 1
Mem. 1
Proc. 1
Mem. 1
Proc. 1
Mem. 1
Unit Crossbar
Segment Crossbar
Full Crossbar

## Slide 33: Hardware costs
Hardware area excluding wires and memory (common to both)
  32-stage RMT: 39.8 square mm
  32-processor dRMT (32-wide VLIW, segment crossbar): 45.5 square mm
  Of the 45.5, 1.74 is due to the crossbar, the rest due to 32 dRMT cores
Overall, our tentative analysis is that hardware costs are comparable
  Tentative because RMT’s numbers are based on 28 nm

## Slide 34: Related Work
Network processors (IXP, Netronome, Quantum Flow)
  Run-to-completion
  Shared memory
  X86-like instructions
  Caches,
  Memory hierarchies,
  General-purpose interconnects,
  Hard to provide determinism
dRMT
Run-to-completion
Shared memory
VLIW instructions with more parallelism
No caches
Single level of memory
Custom crossbar
Compiler solves ILP to provide deterministic latency

## Slide 35: Ongoing and future work
Ongoing work: Implementation in 400G programmable NIC
Future work: State modifications in dRMT
  Run-to-completion allows us to spread state modifications over multiple clock cycles