## Slide 1: dRMT: Disaggregated Programmable Switching
Sharad Chole, Andrew Fingerhut, Sha Ma, Anirudh Sivaraman,
Shay Vargaftik, Alon Berger, Gal Mendelson, Mohammad Alizadeh, Shang-Tse Chuang, Isaac Keslassy, Ariel Orda, and Tom Edsall

## Slide 2: Programmable Switches Today
Match
Action
SRAM/ TCAM
Match
Action
SRAM/ TCAM
Match
Action
SRAM/ TCAM
Resources are aggregated
  Every action needs to paired with a match. Wasted match capacity can not be reclaimed.
  Unused memory in one stage can not be reclaimed by a later stage.

## Slide 3: Problems with aggregation
Large table that does not fit in a single stage’s memory
  Needs to be spread out over multiple stages.
  Action can’t run until the last stage, wasting preceding action units
Performance cliffs:
  Slight increase in requirements suddenly degrades throughput
  E.g., program needs 31 action units, only 30 available
  Pipeline degrades program’s throughput to 1/2, instead of 30/31
Notes: TODO: Need figures