## Slide 1: dRMT: Disaggregated Programmable Switching
Sharad Chole, Andrew Fingerhut, Sha Ma, Anirudh Sivaraman, Shay Vargaftik, Alon Berger, Gal Mendelson, Mohammad Alizadeh, Shang-Tse Chuang, Isaac Keslassy, Ariel Orda, and Tom Edsall
Notes: TODO: Prioritize changes to the compilation part of the talk (compilation + sub-problems + fine-grained deps + proc constraints + animation)

## Slide 2: Today’s Programmable Switches (e.g., RMT)
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In
keys
Pkt Header
results
Pkt Header
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 3: Problems with RMT Architecture
Conflates memory allocation with packet processing
  Wastes processing and/or memory resources
Example: Large table split over multiple stages
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Memory Cluster 1
Memory Cluster 2
Memory Cluster 3
Stage N
Match
Action
Memory Cluster N
Must extract key multiple times
Only last stage executes action
Wastes match/action capacity
Notes: Large table:
* Each stage has to extract and search for the key
* Action cannot be executed until last stage
 Wastes key generation and action capacity

## Slide 4: Problems with RMT Architecture
Forces rigid order on operations: match→action→match→action→…
  Wastes resources for “imbalanced” programs
Example: Tables without a match & default action
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Stage N
Match
Action
Default action
Notes: Large table:
* Each stage has to extract and search for the key
* Action cannot be executed until last stage
 Wastes key generation and action capacity

## Slide 5: Problems with RMT Architecture
Suffers performance cliff if program doesn’t fit
  Recirculate packet to “extend” pipeline → Lowers throughput 2x
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Stage N
Match
Action
Recirculate to ingress
Notes: Large table:
* Each stage has to extract and search for the key
* Action cannot be executed until last stage
 Wastes key generation and action capacity

## Slide 6: Problems with RMT Architecture
Conflates memory allocation with packet processing
Forces rigid order on operations (match→action→match→action→ …)
Suffers performance cliff if program doesn’t fit
The dRMT architecture solves all 3 problems
Key idea:
Disaggregate hardware resources of a programmable switch

## Slide 7: The dRMT Architecture
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 8
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 9
Proc. 1
Proc. 2
Proc. N
Match
Action
Match
Action
Match
Action
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Distributor
Parser
In
Deparser
Pkt 1
Pkt 1
Pkt 2
Pkt 2
Pkt N
Pkt N
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 10
Proc. 1
Proc. 2
Proc. N
Match
Action
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Distributor
Parser
In
Deparser
Pkt 1
Match
Action
Pkt 2
Match
Action
Pkt N
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 11
Proc. 1
Proc. 2
Proc. N
Match
Action
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Distributor
Parser
In
Deparser
Pkt 1
Match
Action
Pkt N+2
Match
Action
Pkt N
Pkt 2
Pkt 2
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 12: dRMT solves problems with RMT
RMT Conflates memory allocation with packet processing
dRMT decouples memory and processors via crossbar
RMT forces rigid order on operations
dRMT enables arbitrary order for operations
RMT suffers performance cliff if program doesn’t fit (recirculation)
dRMT’s throughput degrades gracefully as program size grows

## Slide 13: Two Key Questions
Can dRMT provide deterministic performance?
  Contention at processors, memories, processor/memory interconnect, etc.
Yes! We can preschedule system at compile time to prevent contention entirely.
How much does it cost to build?
  Processor and crossbar area, wiring complexity, etc.
Hardware costs are comparable to RMT. (But dRMT utilizes hardware resources more efficiently.)
Notes: The rest of the talk will look at these questions in more depth.

## Slide 14: Compiling a P4 program to dRMT
Memory : Allocate logical tables to memory clusters
Compute: Schedule respecting dependency and resource constraints
Joint optimization problem in general
  Crossbar decouples the compute and memory problems so long as:
    Compute schedule satisfies constraints on crossbar send side
    Table placement satisfies constraints on receive side (bin packing)
Notes: TODO: Maybe add a figure here.

## Slide 15: dRMT constraints
Resource constraints:
Each processor can generate up to M b-bit-width keys to match against tables
  Each processor can modify up to A packet fields in parallel.
Dependency constraints:
  Operation depending on a match has to wait dM clock cycles
  Operation depending on an action has to wait dA clock cycles
Notes: TODO: Bring back diagram of the processor to explain

## Slide 16: Capturing dependencies in dRMT
Table dependency graph in RMT
Operation dependency graph in dRMT
Routable
Multicast
IGMP
Match
Dep.
Action
Dep.
Routable
Match
Multicast
Match
IGMP
Match
Routable
Action
Multicast
Action
IGMP
Action
dM
dA
dM
dM
dA
Notes: This leads into the compiler.
Toy example very loosely inspired by L2-L3 with Multicast.

## Slide 17: Animation of scheduling problem
M0
A0
A1
1
1
1
M1
1
2
1
1
  N = 2 processors
  Each proc handles a new packet every 2 cycles
  M = 1 (1 match key)
  A = 1 (1 field)
  dM (Match latency) = 2 clock cycles
  dA (Action latency) = 1 clock cycles

## Slide 18: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 19: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1
After dependency constraints alone

## Slide 20: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1
Violates
Action
Constraint

## Slide 21: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 22: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 23: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  | 
 |  |  |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 24: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  | 
 |  |  |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  | 
 |  |  |  |  |  |  | M0 |  | A0 | M1 | x | A1 |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 25: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  | 
 |  |  |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  | 
 |  |  |  |  |  |  | M0 |  | A0 | M1 | x | A1 |  | 
 |  |  |  |  |  |  |  |  | M0 |  | A0 | M1 | x | A1
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 26: ILP formulation of scheduling problem
Assign each operation start time
Dependency constraints
Ensure schedule can be repeated every N cycles w/o violating
resource constraints:
  Create a circle with N equal sectors,
  Assign each operation op to sector (mod N),
  Enforce resource limits on all operations within a sector
- >=
Notes: In this example, we introduced a no-op, but that’s a greedy way of solving it. If we want the optimal schedule, need to solve an ILP.

## Slide 27: Evaluation: Key questions
How efficiently can dRMT utilize hardware resources?
Minimum number of processors to run a P4 program
What happens when hardware resources are insufficient?
Throughput as a function of the number of processors
Is it feasible?
Area cost of dRMT vs. RMT

## Slide 28: Results: switch.p4 on RMT and dRMT
Program | RMT | dRMT | Lower Bound
Ingress | 18 | 15 | 15
Egress | 12 | 7 | 7
Combined | 22 | 21 | 21
Number of processors/stages to run switch.p4 at 1 packet/cycle
dRMT’s gains are most when the program is imbalanced
Notes: Switch.p4 is optimized for RMT.

## Slide 29: dRMT eliminates performance cliffs
Chart: Throughput of switch.p4 egress as the number of processors decreases
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0
RMT | 0.083333 | 0.16667 | 0.25 | 0.33333 | 0.33333 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 1
dRMT | 0.14286 | 0.28571 | 0.42857 | 0.57143 | 0.71429 | 0.85714 | 1 | 1 | 1 | 1 | 1
dRMT’s performance degrades gracefully

## Slide 30: Differences in architecture relative to RMT
Unlike RMT, each dRMT processor needs to store full program
Unlike RMT, we need a scratch pad to store action results for delayed execution
Need to optimize hardware design
  Reduce the number of parallel action fields in a single VLIW from 224 to 32
  Empirically sufficient on switch.p4
Notes: Hardware analysis takeaways:

## Slide 31: Crossbar requirements
Need to connect 32 processors to 32 memory clusters
Each processor can generate up to 8 match keys
Each memory cluster can receive up to 8 match keys
Need multicasting for large tables spread out over multiple memories

## Slide 32: Crossbar designs
Three possible crossbars:
  Unit crossbar: 32*32 crossbar with width to support 8 keys: too restrictive
  Full crossbar: (32 * 8) * (32 * 8) crossbar: too expensive to build
  Segment crossbar: 8 parallel (32*32) crossbars: feasible, with little loss in expressiveness (if tables aren’t split across clusters, equivalent to full)
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Unit Crossbar
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Full Crossbar
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Segment Crossbar

## Slide 33: Hardware cost estimates
Hardware area estimates in 16 nm excluding SerDes and memory
  32-stage RMT: 39.8 square mm (based on RMT estimates at 28 nm, scaled down to 16 nm)
  32-processor dRMT (32-wide VLIW, segment crossbar): 45.5 square mm
  Of the 45.5, 1.74 is due to the crossbar, the rest due to 32 dRMT cores
Notes: TODO: Maybe mention thread count.
Maybe add table from paper.

## Slide 34: Ongoing and future work
Ongoing work: Implementation in programmable NIC
Future work: State modifications in dRMT
  Run-to-completion allows us to spread state modifications over multiple clock cycles

## Slide 35: Enforcing periodic resource constraints
Indicator variables I[op, q, r] to denote whether operation op has quotient q and remainder r when divided by N
=
dividend = divisor * quotient + remainder
= 1
q, r are unique
<= A
action constraints are not violated

## Slide 36: Hardware design for dRMT
()
Packet Header Vector
(4Kb)
VLIW Instruction Table
Config
Table
Crossbar to
Memories
ALU
Thread Select
Scratch
Pad
640b Key
Action Input Selector
(crossbar)
ALU
Action Output Selector
(crossbar)
Op code
Ctrl
… …
8x96b Action
Memory
Match Key Generation (crossbar)

## Slide 37: Problems with RMT Architecture
Conflates memory allocation with packet processing
  Wastes processing and/or memory resources
Example: Parallel table lookups that exceed key gen. capacity of a stage
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Memory Cluster 1
Memory Cluster 2
Memory Cluster 3
Stage N
Match
Action
Memory Cluster N
Must spread tables across multiple stages
Wastes memory capacity

## Slide 38: Related Work
Network processors (IXP, Netronome, Quantum Flow)
  Run-to-completion
  Shared memory
  X86-like instructions
  Caches,
  Memory hierarchies,
  General-purpose interconnects,
  Hard to provide determinism
dRMT
Run-to-completion
Shared memory
VLIW instructions with more parallelism
No caches
Single level of memory
Custom crossbar
Compiler solves ILP to provide deterministic latency