## Slide 1: dRMT: Disaggregated Programmable Switching
Sharad Chole, Andrew Fingerhut, Sha Ma, Anirudh Sivaraman,
Shay Vargaftik, Alon Berger, Gal Mendelson, Mohammad Alizadeh,
Shang-Tse Chuang, Isaac Keslassy, Ariel Orda, and Tom Edsall

## Slide 2: Today’s Programmable Switches (e.g., RMT)
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In
keys
Pkt Header
results
Pkt Header

## Slide 3: dRMT in One Slide
RMT aggregates resources into stages that provide a fixed ratio of memory:match:action
  E.g., A large table spanning two stages consumes two match units
dRMT (disaggregated RMT): disaggregate memory, match, and action resources of a programmable switch. Allocate them independently.
Notes: Say our contribution is the dRMT architecture itself.
TODO: Is there a figure that’s appropriate to this slide?

## Slide 4: The dRMT Architecture
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In

## Slide 5: Memory Disaggregation
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In

## Slide 6: Compute Disaggregation
Proc. 1
Proc. 2
Proc. N
Match
Action
Match
Action
Match
Action
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Distributor
Parser
In
Deparser
Pkt 1
Pkt 1
Pkt 2
Pkt 2
Pkt N
Pkt N

## Slide 7: Compute Disaggregation
Proc. 1
Proc. 2
Proc. N
Match
Action
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Distributor
Parser
In
Deparser
Pkt 1
Match
Action
Pkt 2
Match
Action
Pkt N
Notes: Say that each packet stays at one processor and does not move around.

## Slide 8: Compute Disaggregation
Proc. 1
Proc. 2
Proc. N
Match
Action
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Distributor
Parser
In
Deparser
Pkt 1
Match
Action
Pkt N+2
Match
Action
Pkt N
Pkt 2
Pkt 2

## Slide 9: Problems with RMT Architecture
Conflates memory allocation with packet processing
  Wastes processing and/or memory resources
Example: Large table split over multiple stages
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Memory
Cluster 1
Memory
Cluster 2
Memory
Cluster 3
Stage N
Match
Action
Memory Cluster N
Must extract key multiple times
Wastes match capacity
Action units unused until last stage

## Slide 10: Problems with RMT Architecture
Suffers performance cliff if program doesn’t fit
  Recirculate packet to “extend” pipeline → Lowers throughput 2x
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Stage N
Match
Action
Recirculate to ingress

## Slide 11: dRMT solves problems with RMT
RMT conflates memory allocation with packet processing
dRMT decouples memory and processors via crossbar
RMT suffers performance cliff if program doesn’t fit
dRMT’s throughput degrades gracefully as program size grows
Notes: TODO: Maybe add a figure for each.

## Slide 12: Three Questions
Can dRMT provide deterministic throughput and latency?
Yes. Compiler schedule programs to eliminate contention using an ILP.
How does dRMT compare with RMT on real P4 programs?
Needs fewer processors on open-source, proprietary, random programs.
Are dRMT’s processors and crossbar feasible in hardware?
Yes. dRMT takes up some more area than RMT, mostly due to crossbar.
Notes:   TODO: Spend some time clearly figuring out what to say on this slide. Try and finish up this slide by minute 10.
  Why is first point non-trivial?: Contention at processors and memories.
  Why is second point non-trivial?: Mileage may vary depending on the actual program.
  Why is third point non-trivial?: Crossbar needs to span a large spatial extent (wiring complexity and area overheads). dRMT processors are run-to-completion and store all operations for a packet instead of an RMT stage.
Stuff to say:
1. We designed hardware for the processor+crossbar. We evaluated whether it meets timing and what its area is through synthesis experiments.
Two points to stress:
We can formally show that the throughput of a program on dRMT is at least as good as that of RMT, when normalized to have the same number of hardware resources.
We’ll focus on some of these results through the rest of the talk.

## Slide 13: Compiling a P4 program to dRMT
Proc. 1
Proc. 2
Proc. N
Match
Action
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Pkt 1
Match
Action
Pkt 2
Match
Action
Pkt N
Cycle Packet | 0 | 1 | 2 | 3 | 4 | 5
1 | M |  | A | … |  | 
2 |  |  | M |  | A | …
3 |  |  |  |  | M | …
Cycle Packet | 0 | 1 | 2 | 3 | 4 | 5
1 | M |  | A | … |  | 
2 |  |  | M |  | A | …
3 |  |  |  |  | M | …
Cycle Packet | 0 | 1 | 2 | 3 | 4 | 5
1 | M |  | A | … |  | 
2 |  |  | M |  | A | …
3 |  |  |  |  | M | …
Table placement
Processor scheduling

## Slide 14: Xbar decouples scheduling and placement
RMT couples scheduling and placement.
Can prove that dRMT decouples them under natural conditions:
  Every table is accessed once per packet
  Every processor executes the same schedule with a time offset
Table placement is a variant of bin packing.
Notes: TODO: too much text.
Explain why RMT couples the two problems.
Say that table placement is handled by prior work by Jose et al.
Say that we focus on processor scheduling here
Decouples them in the sense that you can solve them independently and put them together and the solution will:
Work for the joint problem.
No better than any other solution for the joint problem (the non-trivial part).

## Slide 15: Processor Scheduling Example
  2 cycles to complete a match
  1 cycle to complete an action
  Two processors
  Each does 1 match and 1 action per cycle
Proc. 1
Proc. 2
Match
Action
Match
Action
Program Dependencies
Resource Constraints
M0
A0
A1
M1
2
1
1
Notes: TODO: Come up with a better DAG (M1 and A1 can be scheduled in the same clock cycle).
Two main aspects: correctness based on program dependencies, resource constraints based on processors.

## Slide 16: Processor Scheduling Example
Cycle Packet | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
1 | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  |  |  | 
M0
A0
A1
M1
2
1
1
  2 processors handle 1 packet per cycle.
  Packet arrives every 2 cycles per processor.

## Slide 17: Processor Scheduling Example
Cycle Packet | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
1 | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  |  |  | 
2 |  |  | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  | 
M0
A0
A1
M1
2
1
1
  2 processors handle 1 packet per cycle.
  Packet arrives every 2 cycles per processor.
Each processor can only do 1 action per cycle

## Slide 18: Processor Scheduling Example
Cycle Packet | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
1 | M0 |  | A0 | M1 | X | A1 |  |  |  |  |  |  |  | 
M0
A0
A1
M1
2
1
1
  2 processors handle 1 packet per cycle.
  Packet arrives every 2 cycles per processor.
Delay A1 by inserting a no-op

## Slide 19: Processor Scheduling Example
Cycle Packet | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
1 | M0 |  | A0 | M1 | X | A1 |  |  |  |  |  |  |  | 
2 |  |  | M0 |  | A0 | M1 | X | A1 |  |  |  |  |  | 
M0
A0
A1
M1
2
1
1
  2 processors handle 1 packet per cycle.
  Packet arrives every 2 cycles per processor.

## Slide 20: Processor Scheduling Example
Cycle Packet | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
1 | M0 |  | A0 | M1 | X | A1 |  |  |  |  |  |  |  | 
2 |  |  | M0 |  | A0 | M1 | X | A1 |  |  |  |  |  | 
3 |  |  |  |  | M0 |  | A0 | M1 | X | A1 |  |  |  | 
4 |  |  |  |  |  |  | M0 |  | A0 | M1 | X | A1 |  | 
5 |  |  |  |  |  |  |  |  | M0 |  | A0 | M1 | X | A1
M0
A0
A1
M1
2
1
1
  2 processors handle 1 packet per cycle.
  Packet arrives every 2 cycles per processor.

## Slide 21: Minimizing no-ops: ILP formulation
Assign each operation start time
Objective: Minimize max ti
Dependency constraints
Ensure schedule can be repeated every N cycles w/o violating
resource constraints:
  Create a circle with N equal sectors.
  Assign each operation op to sector (mod N).
  Enforce resource limits on all operations within a sector.
- ≥
Notes: In this example, we introduced a no-op, but that’s a greedy way of solving it. If we want the optimal schedule, need to solve an ILP.
Packet that arrived this scheduling period, 1 period in the past, 2 in the past, and so on.
TODO: Show the line wrapping around the circle.

## Slide 22: Evaluation: Comparing RMT and dRMT
P4 Program | RMT | dRMT | Lower bound
switch.p4 ingress | 18 | 15 | 15
Minimum number of processors to run at 1 packet/cycle

## Slide 23: Evaluation: Comparing RMT and dRMT
P4 Program | RMT | dRMT | Lower bound
switch.p4 ingress | 18 | 15 | 15
switch.p4 egress | 12 | 7 | 7
Minimum number of processors to run at 1 packet/cycle

## Slide 24: Evaluation: Comparing RMT and dRMT
P4 Program | RMT | dRMT | Lower bound
switch.p4 ingress | 18 | 15 | 15
switch.p4 egress | 12 | 7 | 7
switch.p4 combined | 22 | 21 | 21
Minimum number of processors to run at 1 packet/cycle

## Slide 25: Evaluation: Comparing RMT and dRMT
P4 Program | RMT | dRMT | Lower bound
switch.p4 ingress | 18 | 15 | 15
switch.p4 egress | 12 | 7 | 7
switch.p4 combined | 22 | 21 | 21
proprietary (normalized) | 2.0 | 1.0 | 1.0
Minimum number of processors to run at 1 packet/cycle
Gains of 4.5% to 50% on real programs.
Gains lowest on balanced programs optimized for RMT.
On 100 random programs, mean gain of 10% (max 30%)
Notes: TODO: Maybe add a figure for random program.
Emphasize: Our gains are quite significant. Switch.p4 is optimized for RMT. We give switch.p4 the benefit of full memory disaggregation.

## Slide 26: dRMT eliminates performance cliffs
Chart: Processors
| 1.0 | 1.0 | 2.0 | 2.0 | 3.0 | 3.0 | 4.0 | 4.0 | 5.0 | 5.0 | 6.0 | 6.0 | 7.0 | 7.0 | 8.0 | 8.0 | 9.0 | 9.0 | 10.0 | 10.0 | 11.0 | 11.0 | 12.0 | 12.0 | 13.0 | 13.0 | 14.0 | 14.0 | 15.0 | 15.0
RMT | 0.08 | 0.083333 | 0.083333 | 0.16667 | 0.16667 | 0.25 | 0.25 | 0.33 | 0.33 | 0.33 | 0.33 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 1 | 1 | 1 | 1 | 1 | 1 | 1
dRMT | 0.14 | 0.29 | 0.43 | 0.57 | 0.71 | 0.86 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 27: dRMT crossbar design
The crossbar is critical to dRMT: Can we build it?
Requirements: 32 processors, 32 memory clusters, 8 keys
Two extremes
  Full crossbar from each processor key to each cluster key
    ((32 * 8) * (32 * 8) crossbar), very flexible, but very costly
  Unit crossbar between each processor and each cluster
    Wide 32*32 crossbar, inflexible, but cheap
Notes: TODO: Maybe add a decent figure
Make the segment crossbar a more prominent contribution
Don’t present all three as equally worthy choices
Multiple keys under a cluster: explain
Make it clear what was clever about us creating this design.
Sub-sub-sub bullets are super-super-superfluous
Add a diagram

## Slide 28: dRMT’s segment crossbar
Segment crossbar: 8 parallel (32 * 32) crossbars
  Compromise between full and unit crossbar
Segment equivalent to full if tables are not split across clusters
  Can assign keys to segments appropriately to achieve equivalence
Notes: TODO: Say that we did a manual place and route for the segment crossbar.

## Slide 29: Comparing areas of RMT and dRMT
dRMT incurs a few squared mm in area.
Chart: Processors/Stages
| 16.0 | 24.0 | 32.0
RMT | 19.9 | 29.9 | 39.8
dRMT | 22.7 | 34.1 | 45.5
Notes: TODO: Add results on random P4 DAGs as well?
Highlight the numbers better. Put dRMT at the middle.
Make a bar chart here

## Slide 30: Summary
dRMT: Disaggregated architecture for programmable switches
Ongoing work: Implementation in programmable NIC
Many open questions
  Scheduling different packet types
  Stateful packet processing
Webpage: http://drmt.technion.ac.il/

## Slide 31: Backup slides

## Slide 32: dRMT eliminates performance cliffs
Chart: Processors/Stages
| 1.0 | 1.0 | 1.99 | 2.0 | 2.99 | 3.0 | 3.99 | 4.0 | 5.0 | 5.0 | 5.99 | 6.0 | 7.0 | 7.0 | 8.0 | 8.0 | 9.0 | 9.0 | 10.0 | 10.0 | 11.0 | 11.0 | 11.99 | 12.0 | 13.0 | 13.0 | 14.0 | 14.0 | 15.0 | 15.0
RMT | 0.083333 | 0.083333 | 0.16667 | 0.16667 | 0.25 | 0.25 | 0.33 | 0.33 | 0.33 | 0.33 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 1 | 1 | 1 | 1 | 1 | 1 | 1
dRMT | 0.14286 | 0.14 | 0.28571 | 0.29 | 0.42857 | 0.43 | 0.57143 | 0.57 | 0.71429 | 0.71 | 0.85714 | 0.86 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 33: Evaluation: switch.p4 on RMT and dRMT
P4 Program | RMT | dRMT | Lower bound
Ingress (switch.p4) | 18 | 15 | 15
Egress (switch.p4) | 12 | 7 | 7
Switch.p4 combined | 22 | 21 | 21
Minimum number of processors to run at 1 packet/cycle
P4 Program | RMT | dRMT (IPC=2) | Lower bound
Ingress (switch.p4) | 360 | 243 | 243
Egress (switch.p4) | 240 | 198 | 197
Switch.p4 combined | 440 | 243 | 243
Minimum number of threads to run at 1 packet/cycle
Notes: Switch.p4 is optimized for RMT.
198 in red is distracting.
Explain briefly what switch.p4 is.
Explain why ingress+egress is not the same as combined.
Explain why combined is not a huge win.
The results seem comparable, not better for dRMT.

## Slide 34: Evaluation: switch.p4 on RMT and dRMT
P4 Program | RMT | dRMT (IPC=1) | dRMT (IPC=2) | Lower bound
Ingress (switch.p4) | 18 | 17 | 15 | 15
Egress (switch.p4) | 12 | 11 | 7 | 7
Switch.p4 combined | 22 | 21 | 21 | 21
Minimum number of processors to run at 1 packet/cycle
P4 Program | RMT | dRMT (IPC=1) | dRMT (IPC=2) | Lower bound
Ingress (switch.p4) | 360 | 245 | 243 | 243
Egress (switch.p4) | 240 | 217 | 198 | 197
Switch.p4 combined | 440 | 243 | 243 | 243
Minimum number of threads to run at 1 packet/cycle
dRMT is near optimal:
Fewest possible processors
Near-ideal (critical path) latency
Comparable on switch.p4 combined, which is optimized for RMT
Notes: Switch.p4 is optimized for RMT.
198 in red is distracting.
Explain briefly what switch.p4 is.
Explain why ingress+egress is not the same as combined.
Explain why combined is not a huge win.
The results seem comparable, not better for dRMT.

## Slide 35: Scheduling Constraints
Processor resource constraints:
Generate up to M b-bit keys to match on per cycle (M=8, b=80)
  Perform actions on up to A packet fields per cycle (A=32)
  Perform match/action on different packets every cycle (Inter-packet concurrency (IPC) = 1 or 2)
Dependency constraints:
  Operation depending on a match (action) has to wait dM (or dA) cycles
Notes: Change this into compiler overview and add a overview diagram P4->DAG->Packet Scheduling. Also simplify constraints. Maybe show constraints in the overview diagram.
TODO: Bring back diagram of the processor to explain
IPC went by too fast. Need to introduce it so that people are not lost. Maybe just call it packet concurrency?
Multi-processor design can lead to reordering. Useful to mention this is not a problem up front because everything has the same latency.
Too much redundancy in the second bullet
TODO: More animations here
Too many details
It wasn’t clear what a key was.
Too many details.
Simplify number of constraints.

## Slide 36: Extracting dependencies from P4 programs
Table dependency graph
Operation dependency graph
Routable
Match
Multicast
Match
IGMP
Match
Routable
Action
Multicast
Action
IGMP
Action
dM
dA
dM
dM
dA
Match
Dep.
Action
Dep.
Routable
Multicast
IGMP
Notes: This leads into the compiler.
Toy example very loosely inspired by L2-L3 with Multicast.
TODO: Might be too detailed.
This part was not very interesting here.
Didn’t get the high-level problem in slide 15. Make it very clear what proc. Scheduling was on slide 15.
Say that you go from P4->Operation dependency graph -> ILP (and then you could say that the P4->ODG transformation is not shown).
Could remove this slide.

## Slide 37: dRMT hardware: instruction memory
A dRMT processor executes/stores an entire program; an RMT stage only executes/stores a program slice.
Must reduce memory required to encode an action.
RMT actions can modify 224 packet fields in parallel; we found 32 sufficient
Chart: Distribution of number of packet fields in switch.p4 actions
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 10.0 | 14.0 | 18.0 | 21.0 | 25.0 | 29.0
Number of primitive actions to execute | 0.056452 | 0.25806 | 0.16935 | 0.15323 | 0.10484 | 0.024194 | 0.032258 | 0.056452 | 0.056452 | 0.040323 | 0.0080645 | 0.016129 | 0.0080645 | 0.0080645 | 0.0080645
Notes: Mention that the lower half is a histogram or empirical distribution
The pdf indicates 29 is sufficient, but you seem to have 32.
Seemed like a jump from eval to design (hardware design)
Some sign posting would help.
Make it clear that the processor has to store the program.

## Slide 38: dRMT architecture: crossbar
The segment crossbar is equivalent to full crossbar if tables are not split across clusters! (see paper for details)
dRMT uses One-to-Many Segment Crossbar
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Unit Crossbar
(0.561 mm2)
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Segment Crossbar
(0.576 mm2)
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Full Crossbar
(4.464 mm2)
Notes: Area numbers for 32x32 crossbar with 8 80-bit keys on each side

## Slide 39: dRMT Match Action Processor
Packet Header Vector
(4Kb)
Packet Header Vector
(4Kb)
Packet Header Vector
(4Kb)
Crossbar to
Memories
Scratch
Pad
8x80b Key
Action Input Selector
(crossbar)
Config
Table
Action Output Selector
(crossbar)
VLIW Instruction Table
Ctrl
Thread Select
8x96b Action
Memory
Match Key Generation (crossbar)
ALU
ALU
Op code
… …
Notes: TODO: This diagram might be too detailed.
Maybe just replace it with a high-level overview slide.
Key differences with RMT:
-- dRMT processor needs to store full program  Config table & instruction table more expensive
-- Scratchpad (store results for delayed execution
-- VLIW Instructions: 32 ALUs instead of 224

## Slide 40: Enforcing periodic resource constraints
Indicator variables I[op, q, r] denote whether top has quotient q and remainder r when divided by N
=
dividend = divisor * quotient + remainder
= 1 (for each op)
q, r are unique
<= A (for each r)
action constraints are not violated (match constraints similar)

## Slide 41: Problems with RMT Architecture
Forces rigid order on operations: match→action→match→action→…
  Wastes resources for “imbalanced” programs
Example: Tables without a match (default action)
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Stage N
Match
Action
Default action
Notes: TODO: Consider removing slide on tables without a match. Technically, we can pack this with another program that *does* use the match. i.e., could combine slide 4 with slide 3.