## Slide 1: dRMT: Disaggregated Programmable Switching
Sharad Chole, Andrew Fingerhut, Sha Ma, Anirudh Sivaraman,
Shay Vargaftik, Alon Berger, Gal Mendelson, Mohammad Alizadeh, Shang-Tse Chuang, Isaac Keslassy, Ariel Orda, and Tom Edsall

## Slide 2: Programmable Switches (e.g., RMT)
Match
Action
Memory
Match
Action
Memory
Match
Action
Memory
Stage 1
Stage 2
Stage N
Notes: TODO: Show packet flow as well through both architectures.

## Slide 3: Resources are aggregated in RMT
RMT couples memory allocation with computations
  Example 1: large match-action table split over multiple stages
  Action can’t execute until last stage; preceding action units unused
Forces match, followed by action order on operations
  Example 2: default actions, match capacity is wasted
Notes: TODO: Is the performance cliff really a result of aggregation?
TODO: Visual of example 1 and maybe example 2.

## Slide 4: dRMT: disaggregated RMT
Match
Action
Memory
Match
Action
Memory
Match
Action
Memory
Stage 1
Stage 2
Stage N

## Slide 5: dRMT: shared memory using crossbar
Match
Action
Memory
Match
Action
Memory
Match
Action
Memory
Stage 1
Stage 2
Stage N

## Slide 6: dRMT: run-to-completion processors
Match
Action
Memory
Match
Action
Memory
Match
Action
Memory
Packet distributor
Processor 1
Processor 2
Processor N
Notes: TODO: packet flow in run-to-completion
1. State memory layout – processing decoupling as a benefit

## Slide 7: Compiling: fine-grained dependencies
P4 captures coarse-grained dependencies between tables in Table Dependency Graph; each node is a table, dependencies are conservative
We use fine-grained dependencies in Operation Dependency Graph with one node for each match/action operation
Node attribute: Number of primitive actions or match key size
Edge attribute: min. latency between operations
  Either the time required to complete a match
  Or the time required to complete an action
Straightforward to generate by extending p4-hlir
Notes: Looks like a multi-processor or network processor. What makes this interesting and different is that we can preschedule it for deterministic latency. This leads into the compiler.
TODO: This slide is about how we represent P4 program for the purpose of the scheduler
TODO: Add figures here.
Start with table dependency graph in P4
And show more fine-grained dependency graph in P4.

## Slide 8: Constraints on the problem
Match resources
Action resources
Bring back diagram of the processor to explain

## Slide 9: Animation of scheduling problem
M0
A0
A1
1
1
1
M1
1
2
1
1
Match/Action capacity: 1 per processor
Notes: At this point you have explained what the DAG is and what the match/action capacity is.
TODO: Also say there are two processors.

## Slide 10: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 11: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1
After dependency constraints alone

## Slide 12: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1
Violates
Action
Capacity

## Slide 13: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 14: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 15: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  | 
 |  |  |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 16: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  | 
 |  |  |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  | 
 |  |  |  |  |  |  | M0 |  | A0 | M1 | x | A1 |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 17: Animation of scheduling problem
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  |  |  | 
 |  |  |  |  | M0 |  | A0 | M1 | x | A1 |  |  |  | 
 |  |  |  |  |  |  | M0 |  | A0 | M1 | x | A1 |  | 
 |  |  |  |  |  |  |  |  | M0 |  | A0 | M1 | x | A1
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 18: The general compilation problem
Each processor handles a new packet every N cycles (N procs)
Schedule each operation so that schedule can be repeated every N cycles
Can be formulated as an ILP
Notes: We are going to assume one packet per clock cycle. It’s easy to extend it to more general throughputs.
TODO: Replace all the text with a figure.

## Slide 19: ILP formulation
Assign each operation a start time relative to the first operation
Group operations into buckets based on the reminder when the operation start time is divided by N.
Total match/action requirements in a bucket <= match/action capacity
Dependencies must be satisfied between operations
Notes: TODO: Show this idea of scheduling on a circle of length N.
Periodic schedule is just the schedule on a circle, as opposed to a line.
What does the periodic schedule even mean? Show the previous example on a circle.
The reason you can do this as an ILP is you can take any time slot and write it as t*P + Q.
This is how you can formulate as ILP.

## Slide 20: Results: switch.p4 on RMT and dRMT
Program | RMT | dRMT | Lower Bound
Ingress | 18 | 15 | 15
Egress | 12 | 7 | 7
Combined | 22 | 21 | 21
Minimum number of processors/stages to run switch.p4 at 1 packet per cycle
Notes: TODO: When you combine because it’s a bit more balanced, that’s why RMT does better.
Switch.p4 is optimized for RMT.

## Slide 21: dRMT eliminates performance cliffs
Chart: Throughput of switch.p4 egress as the number of processors decreases
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0
RMT | 0.083333 | 0.16667 | 0.25 | 0.33333 | 0.33333 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 1
dRMT | 0.14286 | 0.28571 | 0.42857 | 0.57143 | 0.71429 | 0.85714 | 1 | 1 | 1 | 1 | 1

## Slide 22: Hardware design for dRMT
Unlike RMT, each dRMT processor needs to store full program
Unlike RMT, we need a scratch pad to store action results for delayed execution
Need to optimize hardware design
  Reduce the number of parallel action fields in a single VLIW from 224 to 32
  Empirically sufficient on switch.p4
  If not, spread action over multiple cycles
Notes: TODO: Add an architecture diagram
Make the high-level point that these are the differences between dRMT and RMT.
Slide needs a figure + few panes/bullets that emphasize the differences
Hardware analysis takeaways:

## Slide 23: Crossbar analysis
Need to connect 32 processors to 32 memory clusters
Each processor can generate up to 8 match keys
Each memory cluster can receive up to 8 match keys
Need multicasting for large tables spread out over multiple memories
Three possible crossbars:
  Unit crossbar: 32*32 crossbar with width to support 8 keys: too restrictive
  Full crossbar: (32 * 8) * (32 * 8) crossbar: too expensive to build
  Segment crossbar: 8 parallel (32*32) crossbars: feasible, with little loss in expressiveness
Notes: In fact, we can prove that when there’s no multicast
TODO: Sharad’s pictures for the crossbars might be helpful.
Or try a better set of pictures.
State this result that the segmented crossbar is equivalent to the full crossbar.
We need to find a good way to explain that.

## Slide 24: Hardware costs
Hardware area excluding wires and memory (common to both)
  32-stage RMT: 39.8 square mm
  32-processor dRMT (32-wide VLIW, segment crossbar): 45.5 square mm
Overall, our tentative analysis is that hardware costs are comparable
  Tentative because RMT’s numbers are based on 28 nm

## Slide 25: Related Work
Network processors (IXP, Netronome, Quantum Flow)
  Run-to-completion
  Shared memory
  X86-like instructions
  Caches,
  Memory hierarchies,
  General-purpose interconnects,
  Hard to provide determinism
dRMT
Run-to-completion
Shared memory
VLIW instructions with more parallelism
No caches
Single level of memory
Custom crossbar
Compiler solves ILP to provide deterministic latency

## Slide 26: Ongoing and future work
Ongoing work: Implementation in 400G programmable NIC
Future work: State modifications in dRMT
  Run-to-completion allows us to spread state modifications over multiple clock cycles