## Slide 1: dRMT: Disaggregated Programmable Switching
Sharad Chole, Andrew Fingerhut, Sha Ma, Anirudh Sivaraman, Shay Vargaftik, Alon Berger, Gal Mendelson, Mohammad Alizadeh, Shang-Tse Chuang, Isaac Keslassy, Ariel Orda, and Tom Edsall
Notes: TODO: Prioritize changes to the compilation part of the talk (compilation + sub-problems + fine-grained deps + proc constraints + animation)

## Slide 2: Today’s Programmable Switches (e.g., RMT)
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In
keys
Pkt Header
results
Pkt Header
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 3: Problems with RMT Architecture
Conflates memory allocation with packet processing
  Wastes processing and/or memory resources
Example: Large table split over multiple stages
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Memory Cluster 1
Memory Cluster 2
Memory Cluster 3
Stage N
Match
Action
Memory Cluster N
Must extract key multiple times
Only last stage executes action
Wastes match/action capacity
Notes: Large table:
* Each stage has to extract and search for the key
* Action cannot be executed until last stage
 Wastes key generation and action capacity

## Slide 4: Problems with RMT Architecture
Forces rigid order on operations: match→action→match→action→…
  Wastes resources for “imbalanced” programs
Example: Tables without a match (default action)
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Stage N
Match
Action
Default action
Notes: Consider removing slide on tables without a match. Technically, we can pack this with another program that *does* use the match.

## Slide 5: Problems with RMT Architecture
Suffers performance cliff if program doesn’t fit
  Recirculate packet to “extend” pipeline → Lowers throughput 2x
Stage 1
Stage 2
Stage 3
Match
Action
Match
Action
Match
Action
Stage N
Match
Action
Recirculate to ingress
Notes: Large table:
* Each stage has to extract and search for the key
* Action cannot be executed until last stage
 Wastes key generation and action capacity

## Slide 6: Problems with RMT Architecture
Conflates memory allocation with packet processing
Forces rigid order on operations (match→action→match→action→ …)
Suffers performance cliff if program doesn’t fit
The dRMT architecture solves all 3 problems
Key idea:
Disaggregate hardware resources of a programmable switch

## Slide 7: The dRMT Architecture
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 8
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 9
Proc. 1
Proc. 2
Proc. N
Match
Action
Match
Action
Match
Action
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Distributor
Parser
In
Deparser
Pkt 1
Pkt 1
Pkt 2
Pkt 2
Pkt N
Pkt N
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 10
Proc. 1
Proc. 2
Proc. N
Match
Action
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Distributor
Parser
In
Deparser
Pkt 1
Match
Action
Pkt 2
Match
Action
Pkt N
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 11
Proc. 1
Proc. 2
Proc. N
Match
Action
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Distributor
Parser
In
Deparser
Pkt 1
Match
Action
Pkt N+2
Match
Action
Pkt N
Pkt 2
Pkt 2
Notes: - Each stage has a local memory cluster
- As a packet enters each stage, the “match unit” extracts search keys from the packet header; sends to the local memory cluster for lookup

## Slide 12: dRMT solves problems with RMT
RMT Conflates memory allocation with packet processing
dRMT decouples memory and processors via crossbar
RMT forces rigid order on operations
dRMT enables arbitrary order for operations
RMT suffers performance cliff if program doesn’t fit (recirculation)
dRMT’s throughput degrades gracefully as program size grows

## Slide 13: Two Key Contributions
Can dRMT provide deterministic performance?
  Contention at processors, memories, processor/memory interconnect, etc.
We can schedule system at compile time to prevent contention.
How much does it cost to build?
  Processor and crossbar area, wiring complexity, etc.
Hardware costs are comparable to RMT.
(But dRMT utilizes hardware resources more efficiently.)
Notes: The rest of the talk will look at these questions in more depth.

## Slide 14: Compiling a P4 program to dRMT
Table Placement
Processor scheduling
Crossbar decouples the two problems
Match
Action
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Match
Action
Match
Action
Proc. 1
Proc. 2
Proc. N
?
?
?
Notes: Could provide more intuition for this decoupling.

## Slide 15: Scheduling Constraints
Processor resource constraints:
Generate up to M b-bit keys to match on per cycle (M=8, b=80)
  Perform actions on up to A packet fields per cycle (A=32)
  Perform match/action on IPC packets per cycle (IPC=1 or 2)
Dependency constraints:
  Operation depending on a match has to wait dM cycles (dM=22)
  Operation depending on an action has to wait dA cycles (dA=2)
Notes: TODO: Bring back diagram of the processor to explain

## Slide 16: Modeling dependencies
Table dependency graph
Operation dependency graph
Routable
Match
Multicast
Match
IGMP
Match
Routable
Action
Multicast
Action
IGMP
Action
dM
dA
dM
dM
dA
Match
Dep.
Action
Dep.
Routable
Multicast
IGMP
Notes: This leads into the compiler.
Toy example very loosely inspired by L2-L3 with Multicast.

## Slide 17: Scheduling Example
M0
A0
A1
1
1
1
M1
1
2
1
1
  Each match → 1 key
  Each action → 1 field
  dM (Match latency) = 2 cycles
  dA (Action latency) = 1 cycles
  N = 2 processors
  M (Match capacity) = 1 key per cycle
  A (Action capacity) = 1 field per cycle
  IPC (Concurrency) = 1 pkt per cycle
Proc. 1
Proc. 2
Match
Action
Match
Action

## Slide 18: Scheduling Example
  Focus on 1 processor
  1 packet arrives every 2 cycles
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
M0
A0
A1
1
1
1
M1
1
2
1
1
Notes: TODO: Talk about why focusing on one processor is sufficient.

## Slide 19: Scheduling Example
  Focus on 1 processor
  1 packet arrives every 2 cycles
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 20: Scheduling Example
  Focus on 1 processor
  1 packet arrives every 2 cycles
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | A1 |  |  |  |  |  |  | 
Violates action capacity
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 21: Scheduling Example
  Focus on 1 processor
  1 packet arrives every 2 cycles
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | X | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | X | A1 |  |  |  |  |  | 
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 22: Scheduling Example
  Focus on 1 processor
  1 packet arrives every 2 cycles
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | M0 |  | A0 | M1 | X | A1 |  |  |  |  |  |  |  | 
 |  |  | M0 |  | A0 | M1 | X | A1 |  |  |  |  |  | 
 |  |  |  |  | M0 |  | A0 | M1 | X | A1 |  |  |  | 
 |  |  |  |  |  |  | M0 |  | A0 | M1 | X | A1 |  | 
 |  |  |  |  |  |  |  |  | M0 |  | A0 | M1 | X | A1
M0
A0
A1
1
1
1
M1
1
2
1
1

## Slide 23: ILP formulation of scheduling problem
Assign each operation start time
Objective: Minimize max ti
Dependency constraints
Ensure schedule can be repeated every N cycles w/o violating
resource constraints:
  Create a circle with N equal sectors,
  Assign each operation op to sector (mod N),
  Enforce resource limits on all operations within a sector
- ≥
Notes: In this example, we introduced a no-op, but that’s a greedy way of solving it. If we want the optimal schedule, need to solve an ILP.

## Slide 24: Evaluation: switch.p4 on RMT and dRMT
P4 Program | RMT | dRMT (IPC=1) | dRMT (IPC=2) | Lower bound
Ingress (switch.p4) | 18 | 17 | 15 | 15
Egress (switch.p4) | 12 | 11 | 7 | 7
Switch.p4 combined | 22 | 21 | 21 | 21
Minimum number of processors to run at 1 packet/cycle
P4 Program | RMT | dRMT (IPC=1) | dRMT (IPC=2) | Lower bound
Ingress (switch.p4) | 360 | 245 | 243 | 243
Egress (switch.p4) | 240 | 217 | 198 | 197
Switch.p4 combined | 440 | 243 | 243 | 243
Minimum number of threads to run at 1 packet/cycle
dRMT is near optimal; to run at line-rate:
Fewest possible processors
Near-ideal (critical path) latency
Notes: Switch.p4 is optimized for RMT.

## Slide 25: dRMT eliminates performance cliffs
Throughput vs. Processors for switch.p4 egress

## Slide 26: dRMT Match Action Processor
Packet Header Vector
(4Kb)
Packet Header Vector
(4Kb)
Packet Header Vector
(4Kb)
Crossbar to
Memories
Scratch
Pad
8x80b Key
Action Input Selector
(crossbar)
Config
Table
Action Output Selector
(crossbar)
VLIW Instruction Table
Ctrl
Thread Select
8x96b Action
Memory
Match Key Generation (crossbar)
ALU
ALU
Op code
… …
Notes: Key differences with RMT:
-- dRMT processor needs to store full program  Config table & instruction table more expensive
-- Scratchpad (store results for delayed execution
-- VLIW Instructions: 32 ALUs instead of 224

## Slide 27: Hardware area estimates (mm2)
Number of Processors | RMT | Crossbar with 32 memory clusters | dRMT(IPC=1) with crossbar | dRMT(IPC=2) with crossbar
16 | 19.9 | 0.857 | 17.7 | 22.7
24 | 29.9 | 1.254 | 26.6 | 34.1
32 | 39.8 | 1.740 | 35.5 | 45.5
dRMT hardware cost is comparable to RMT.
Notes: TODO: Add results on random P4 DAGs as well?

## Slide 28: Summary
dRMT: Disaggregated architecture for programmable switches
Ongoing work: Implementation in programmable NIC
Many open questions
  Scheduling different packet types
  Stateful packet processing
Webpage: http://drmt.technion.ac.il/

## Slide 29: Backup slides

## Slide 30: Enforcing periodic resource constraints
Indicator variables I[op, q, r] denote whether top has quotient q and remainder r when divided by N
=
dividend = divisor * quotient + remainder
= 1 (for each op)
q, r are unique
<= A (for each r)
action constraints are not violated (match constraints similar)

## Slide 31: Crossbar designs
The segment crossbar is equivalent to full crossbar if tables are not split across clusters! (see paper for details)
dRMT uses One-to-Many Segment Crossbar
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Unit Crossbar
(0.561 mm2)
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Segment Crossbar
(0.576 mm2)
Proc. 1
Mem. 1
Proc. 2
Mem. 2
Full Crossbar
(4.464 mm2)
Notes: Area numbers for 32x32 crossbar with 8 80-bit keys on each side