## Slide 1: dRMT: Disaggregated Programmable Switching
Sharad Chole, Andrew Fingerhut, Sha Ma, Anirudh Sivaraman,
Shay Vargaftik, Alon Berger, Gal Mendelson, Mohammad Alizadeh, Shang-Tse Chuang, Isaac Keslassy, Ariel Orda, and Tom Edsall

## Slide 2: Programmable Switches (e.g., RMT)
Match
Action
Memory
Match
Action
Memory
Match
Action
Memory
Stage 1
Stage 2
Stage N

## Slide 3: Resources are aggregated in RMT
Resources unused in one stage can’t be reclaimed in another
Example 1: large match-action table split over multiple stages
  Action can’t execute until last stage; preceding action units unused
Example 2: default actions
  Match capacity is wasted
Notes: TODO: Is the performance cliff really a result of aggregation?

## Slide 4: dRMT: disaggregated RMT
Match
Action
Memory
Match
Action
Memory
Match
Action
Memory
Stage 1
Stage 2
Stage N

## Slide 5: dRMT: shared memory using crossbar
Match
Action
Memory
Match
Action
Memory
Match
Action
Memory
Stage 1
Stage 2
Stage N

## Slide 6: dRMT: run-to-completion processors
Match
Action
Memory
Match
Action
Memory
Match
Action
Memory
Packet distributor
Processor 1
Processor 2
Processor N

## Slide 7: Compiling to the dRMT architecture
Given a P4 program.
Generate a periodic schedule of operations across processors without violating resource constraints (e.g., match capacity, action capacity, and memory capacity)

## Slide 8: Compiling: fine-grained dependencies
P4 captures coarse-grained dependencies between tables in its Table Dependency Graph; each node is a table
We use fine-grained dependencies in Operation Dependency Graph with one node for each match/action operation
Node attribute: Number of primitive actions or match key size
Edge attribute: min. latency between operations
  Either the time required to complete a match
  Or the time required to complete an action

## Slide 9: Operation Dependency Graph
Straightforward to generate by extending p4-hlir
TODO: Insert figure from paper

## Slide 10: The compilation problem
Each processor handles a new packet every N cycles (N procs)
Schedule each operation so that schedule can be repeated every N cycles
  Assign each operation a start time relative to the first operation
  Group operations into buckets based on the reminder when the operation start time is divided by N.
  Total match/action requirements in a bucket <= match/action capacity
  Dependencies must be satisfied between operations
Can be formulated as an ILP
Notes: We are going to assume one packet per clock cycle. It’s easy to extend it to more general throughputs.

## Slide 11: Animation of compilation

## Slide 12: Result: table from papers

## Slide 13: Results: performance cliffs
Cyclic scheduling

## Slide 14: Hardware costs of dRMT

## Slide 15: Future work